Lecture 38 Traffic Characteristics

There are several terms that are important to understanding traffic flow and operations.

- Spot speed – instantaneous speed at a given point.

- Time mean speed – mean speed of n vehicles passing a point.

- Space mean speed – geometric mean over a section of road

- Overall speed – speed including stops over some distance

- Running speed – speed over some distance without stops

Traffic Volume Characteristics

Volume is the number of vehicles that pass a point per unit of time.  Expressed as

Average Daily Traffic

DT is the daily traffic and n is the number of days of the count

Annual Average Daily Traffic Michigan Map

This count reflects the entire year.

Design Hourly Volume

This value is selected as some percent of the AADT usually the 30th highest hourly volume.  Typically it is about 15% of AADT.  Figure 16.3 shows the curves for % ADT vs number of hours exceeded.  Note that the 30th hour is only 0.3% of the hours in a year.

Traffic volume is not a constant and is constantly changing.  It varies with location, time of day, day of week and month of the year.

Peak Hour Factor

PHF is the hourly volume divided by n times the highest n period of the hour.  For example if the volume is 4000 vph and the highest 15 min is 1100 vehicles the

This value is used in capacity analysis .