# Lecture 3 Geometric Design (Chap 16) – based on consideration of environment, safety, consistency and economy

Factors that influence geometric design standards - See AASHTO Policy on Geometrics Design of Highways and Streets 2001.

Functional classification-Arterial, collector and local access (or subdivisions)

Traffic volume - ADT and DHV

Design speed

Topography/terrain

Level

Rolling

Mountainous

Definitions

AADT =

# ADT =

# DHV - Design Hourly Volume approximately 15% of AADT usually determined as the 30th highest hourly volume. This means over 99% of annual traffic volume are less then the DHV.

Design speed - maximum safe speed that can be maintained over a section of highway when design features control (alignment, grade, etc).  Design Speed is selected as a function of classification, ADT and terrain.  See the tables in the AASHTO design Guide or the text book

Level terrain = sight distance is long or could be made so without difficulty

Rolling terrain = natural slopes consistently rise above or below grades with occasional steep slope

Mountainous terrain = longitudinal and transverse changes in elevation of the ground with respect to the road are abrupt and where benching and side hill excavation are required.

# Cross Section Elements (See Sketch below)

Roadway (traveled way) = 12 ft

Shoulder = 10 ft

Cross slope = 1.5-2% or

Fore slope = 1on 6 to I on 4

Back slope = 1 on 2 or more

Clear zone distance = 30 ft

Hinge point = break at edge of shoulder and fore slope

Ditch = Depth to bottom in relation to the plan grade

# Medians = Min in urban area 30 ft

# Edge of Metal = edge of the paved surface

# A Calculator to find typical design criteria is found at Calculator for Design Criteria