# Lecture 4 Vertical Alignment

Controlled by vehicle performance, safety (sight distance), and drainage

Vehicle performance - Related to the size and power of the vehicle. The usual is for a truck with Weight/HP = 300 or metric equivalent. Performance curves are in the AASHTO Design Guide or Fig 3.5. Maximum grades are developed from these curves and requirement that reduction in speed is less than 10 mph. To determine the maximum grade for a given road consult the Design Guide. Typical values for several different conditions are given in Table 16.4 p 690.  As a matter of operational considerations it is better to have steep grades at the bottom of long compound grades

Safety consideration – Safety is based on the ability of the driver to see over a crest vertical curve or lighted region on a sag vertical curve.

Vertical curve calculation requires that vertical curve characteristics be known based on the following development.

# Using boundary conditions

G1 and G2 are the grades entering and leaving the VC

The high point or low point on the VC can be calculated from the equation

A Calculator for determining the properties of a vertical curve is available at the link Calculator for Vertical Curve Properties

In order to precede it is necessary to determine the stopping distance. This is calculated in the following manner

# Summing forces parallel to the plane of the vehicle

S in the equations above is the stopping distance (meters) for level roads and f = 3.4/9.81=0.34.

The English version of the equations is

If there is a grade to consider use the equation with the grade term G or use a Calculator for stopping sight distance available at Calculator for Stopping Sight Distance

The following Table gives the stopping distance for level wet pavements.

English values for stopping distance without grade are given in Table 16.5 p698.

Another method of calculating braking distance is to consider aerodynamic resistance, braking efficiency and rolling resistance as presented in Principles of Highway Engineering and Traffic Analysis by Mannering and Kilareski. The distance calculated using this technique is shorter than using the constants deceleration technique by about 5 – 10 %.  The significant equation is

gb = 1.04 for cars

hb = braking efficiency = 1

m = road adhesion = 0.5 to 0.8

fr = rolling resistance = 0.2

W = weight lbs

V = speed fps

Ka = air resistance = r/2CdAf

R = density of air = 0.0024 slugs/ft3

Cd = 0.25

Af = frontal area ft2o

Sin(f) = slope of road in percent

# Occasionally it is necessary to determine the passing sight distance associated with a road section.  A Calculator for determining passing sight distance

# is available at the link Calculator for Passing Sight Distance