## Slide 1: EE 3170 Lecture 8
The Stack and Subroutines

## Slide 2: Lecture 8 Concepts
Lecture 8 covers Chapter 5 of the book, plus a whole bunch of stuff.
The Stack
  What is it, how is it used, what are the instructions that are associated with the stack…
Subroutines
  What are they, how do we invoke them, what happens to the hardware when we call one, how do we pass data back and forth to a subroutine…

## Slide 3: Stacks
Stack
  A Dynamic Data Structure
  Access is strictly Last-In-First-Out (LIFO)
  Structure:

## Slide 4: Stacks
Stack Access Operations
  Push – Put new item on top of the stack
  Pop – Remove the top item from stack
Microprocessor Interpretation
  Stack is a contiguous set of memory
  Push – Copy data from a register into the next available word above current top
    New word becomes new top of stack
  Pop – Move data from top word in stack into a register
    Next word down in the stack becomes new top
    Value of previous top is lost to the stack

## Slide 5: Stack Management
Address of the top of the stack changes with each Push or Pop
Stack Pointer (SP) register
  Holds address of the first empty word above the top of stack
SP must be incremented or decremented with each Push or Pop
  This is done automagically by the hardware.

## Slide 6: Stack Management
Stack Location in Memory
  Stack Size changes as program runs
    Push increases stack size
    Pop decreases stack size
  Code usually starts at a low address and grows into higher addresses
  Therefore, stack starts at a high address and grows into lower addresses.
  All stack management is done for you, once you tell the HC11 where the stack starts.

## Slide 7: 68HC11 Stack Management
In 68HC11:
  Pops are called Pull
  ISA predates the standardization of the term Pop
8-bit Push and Pull instructions
  psha pshb
  pula pula

## Slide 8: 68HC11 Stack Management
16-bit Push and Pull instructions
  pshx pshy
  pulx puly
  Low-order byte goes to stack first.
There is no pshd or puld
  D = A:B
  Can emulate pshd with pshb and psha
  Similarly, emulate puld with pula and pulb

## Slide 9: 68HC11 Stack Management
Stack Pointer Manipulation
  lds and sts
    Load and Store SP
    Used to initialize SP
  ins and des
    Increment and Decrement SP
    NOT needed during normal PSHx and PULx instructions
  tsx, txs, tsy, tys
    Transfer (copy) between SP and X or Y

## Slide 10: 68HC11 Stack Example
Swap contents of A and B using stack as swap buffer
  ldaa #$00 ldab #$FF psha ; RegA -> stack pshb ; RegB -> stack pula ; stack -> RegA pulb ; stack -> RegB
(Software demo)

## Slide 11: Subroutines
A.K.A:
  Procedure, Function, Method
Reusable program module
  Write it once
  Store it once
  Invoke it from the main program
  When finished it returns to the main program
A sequence of instructions that look like one instruction in the main source-code
  e.g., call label-of-subroutine

## Slide 12: Desirable Properties
Independence
  Subroutine and main program may be written independently
    Subroutine does not refer to addresses or labels defined in the main program
    and vice-versa (except for the first instruction)
  Subroutine and main program can be assembled independently and linked at loading time

## Slide 13: Subroutine Call
Main program transfers control to the subroutine
  Can be anywhere in the main code
What does this mean, practically?
  PC  address of first instruction in subroutine

## Slide 14: Subroutine Return
Returning From a Subroutine
  Subroutine transfers control back to the main program
Again, what does this mean?
  PC  address of first instruction after the calling instruction

## Slide 15: Subroutine Definitions
Nesting – One subroutine calls another subroutine
Nesting Level – Number of calls needed to reach a routine
  Level 0 – Main program
  Level 1 – Subroutine called by main program
  Level 2 – Subroutine called by a Level 1 routine
  Level k – Subroutine called by a Level k-1 routine

## Slide 16: Subroutine Definitions
Parent – The routine executing the call instruction (caller)
Child – the called routine (callee)
Return Address – Address of instruction in parent program to which the child returns
  Just after the call instruction
  PC incremented during fetch of call

## Slide 17: Subroutine Definitions
Parameters – Data passed from parent to child
Return Values – Data passed from child to parent
Recursion – When a subroutine calls itself
  Subroutine is its own parent and child
  Example, factorial N! = N x (N-1)!

## Slide 18: Subroutine Linkage
Subroutine Linkage – Process of:
  Passing parameters and return values between parent and child
  Saving and restoring the return address

## Slide 19: Calling Convention
Calling Convention – Protocol to implement the linkage
  Defines actions for call and return
  Assigns responsibilities to parent and child
  Must be strictly obeyed OR ELSE
    Data could get lost or corrupted
    Return address could get lost or corrupted

## Slide 20: Return Address Linkage
Where do we store the return address?
  Don’t want to use a register
    Inhibits nesting and recursion
  Don’t want to use a fixed static memory location
    Inhibits nesting and recursion
    Subroutine would have to know parent’s label
  It is temporary
    Only needed until return
    Would like to liberate that memory when done
Stack is the obvious choice.
  Well, maybe not totally obvious, but it’s the best choice anyways. Trust me, I’m a professional.

## Slide 21: 6811 Call Instructions
Two Call Instructions
  bsr addr – Branch to subroutine starting at address addr
    Relative addressing (short range)
  jsr addr – Jump to subroutine starting at address addr
    Direct, Extended, or Indexed addressing

## Slide 22: 6811 Call Instruction Actions
Actions
  Push PC onto stack (Return address)
    Remember this is done automatically.
  PC  addr (actually the calculated effective address)

## Slide 23: 6811 Return Instruction
One return Instruction
  rts = Return from Subroutine
Actions
  Pops stack to PC (return address)
    PC  Previously pushed return address
      Hopefully!
    Next instruction fetched will be instruction after the Call

## Slide 24: Achtung!
Subroutine could use the stack while running.
Subroutine must be careful to pop everything it pushes.
  “Take only pictures, leave only footprints.”
  Make sure the stack is the same as when the subroutine was called.
We need the return address to be at the top of the stack for rts instruction

## Slide 25: Calling Convention Types
Types are based on how data is passed between parent and child.
We have three basic ideas:
  1. Register-based – Data passed in registers
  2. Memory-based – Data passed in a fixed memory area
    Usually the memory space immediately following the call
    Management gets a little tricky

## Slide 26: Calling Conventions…
3. Stack-based – Data passed in the stack
  Everybody knows where the stack is
    (SP tells them)
  Stack expands and shrinks with demand. (Bonus!)

## Slide 27: Register-Based Calling
Parent
  Stores parameters in registers
  Calls child
Child
  Uses parameters stored in registers
  Stores return values in registers
  Returns to parent
Parent
  Uses return values in registers

## Slide 28: A Programming Problem
Example: Summation (1 to N)
Realistically, this is a dumb problem. You wouldn’t use any of these methods. You would simply use the formula sum=((n+1)n)/2.
Remember, stop and think about your problem!

## Slide 29: Register-Based Calling, p. 3
Parent
  …
  ldab #N
  jsr adds
  …
Child
adds clra ; sum = 0 tstb ; set CCs w/B loop beq retn ; while b != 0 aba ; sum = sum + i decb ; i = i-1 bra loop retn rts

## Slide 30: Pros and Cons…
Advantages
  Very fast (no extra load or store)
  Pretty easy too.
Disadvantages
  May have more parameters than available registers
    Given that we have a whopping 4 registers in the HC11, this is extremely likely.
  Nested Calls
    Require more registers
    Must coordinate register usage between subroutines
  Recursion
    Child wants same registers as parent
    Parent must move parameters before calling child

## Slide 31: Memory-Based Calling
Parent
  Store parameters in Data Link Area in memory
    Usually the memory words right after the call
  Call child

## Slide 32: Memory-Based Calling
Child
  get return address from the stack
  access parameters using offset from return address
  Store any return values using offset
  Return to parent
Parent
  Load return values from Data Link Area

## Slide 33: Memory-Based Calling
Parent
  … ldab #N stab LNK jsr adds LNK rmb 1 ; Reserve Multiple Bytes ldaa LNK …
Child
  adds pulx ; get base for LNK inx ; correct ret addr pshx ; restore ret addr clra ; sum = 0 ldab -1,X ; get val of N loop beq retn ; while b != 0 aba ; sum = sum + i decb ; i = i-1 bra loop retn staa -1,X ; save sum rts

## Slide 34: Memory-Based Calling
Advantages
  Arbitrary number of parameters
  Some ISAs do this efficiently
Disadvantages
  Slower (more loads and stores)
  Requires mixing of instructions and data in memory (BAD!!)
  Complex
    jsr does not actually store the return address
    Subroutine must adjust and re-push the return address
    Very easy to mess this one up

## Slide 35: Stack-Based Calling
Parent
  Pushes parameters onto stack
  Calls child
    No address passing - address is in SP
Child
  Pops return address to safe place
    Usually the X or Y register
  Pops parameters off stack
  Pushes return values on stack
  Re-pushes return address on stack
  Returns to parent
Parent
  Pops returned values off stack

## Slide 36: Stack-Based Calling
Parent
  … ldab #N pshb jsr adds pula …
Child adds pulx ; save RA clra ; sum = 0 pulb ; get N loop beq return ; while b != 0 aba ; sum = sum + i decb bra loop return psha ; save sum pshx ; push RA rts

## Slide 37: Stack-Based Calling
Advantages
  Arbitrary number of parameters
  No need to know storage location at assembly time
  Nested Calls
    Each routine builds on previous stack
    Each routine has its storage space
  Recursion
    Same as any other nested call
Disadvantages
  Slower - still have to load and store

## Slide 38: Comments on Calling
Register-based conventions are fastest and simplest.
However, stack-based are preferred.
  Flexible and predictable
We have avoided a few complexities so far
  What if:
    Parent has data stored in a register
    Child wants to use that register
  Nesting and recursion are complex.

## Slide 39: Lecture 8 Summary
The stack is a dynamic data structure mostly maintained by the hardware.
You need to initialize the stack pretty much all the time.
Pushing puts data on the top of the stack.
Pulling takes data off the top of the stack.

## Slide 40: Lecture 8 Summary
Subroutines are called by jsr or bsr and returned from by rts.
Three different calling conventions:
  Register-based
  Memory-based
  Stack-based
The one you pick isn’t as important as just doing it carefully.