## Slide 1: EE 3170 Lecture 2
Chapter 1 - Digital Computer Fundamentals

## Slide 2: Chapter 1 Concepts
Numeric Representation Quick Review
Flip-flops and Registers
Memory
Basic Instruction-Controlled, Stored-Program Processors
  Structure
  Operation

## Slide 3: Numeric Representation
We spent a lot of time in EE 2171 talking about these.
Important ones:
  Unsigned
  Two’s Complement
  BCD
All of these can be expressed in shorthand: octal or hex.

## Slide 4: Unsigned Binary
Evaluate each bit as a power of 2.
Example:
  b101010 = 25+23+21 = 32 + 8 + 2 = 42
Range:
  0 -> 2n-1
  E.g., if n = 4, range is 0-15.

## Slide 5: Two’s Complement
MSB becomes sign bit
  0 - Positive
  1 - Negative
If the number is negative, we need to:
  Flip all bits, and add 1
  Then do the normal binary->decimal conversion
If the number is positive:
  Just do the conversion
Range:
  -2n-1 -> 2n-1-1
  E.g., if n = 4, range is -8 to +7

## Slide 6: BCD
Replace each decimal digit with a 4-bit binary pattern.
Some patterns are unused.
Math kinda sucks.
We mention this because the HC11 supports BCD arithmetic.

## Slide 7: It’s Deep
To quote a famous philosopher, “Remember: Your focus determines your reality.”
The value stored in a computer is simply a bunch of 1’s and 0’s. It’s up to you to assign meaning to those 1’s and 0’s!

## Slide 8: Octal and Hex
Octal replaces three bits with a single digit from 0-7.
Hex replaces four bits with a single digit from 0-F.
Motorola data widths are 8 and 16 bits. Thus, we spend a lot of time dealing with hex this semester.

## Slide 9: Motorola Number Prefixes
For Hex: $
  0xBEEF = $BEEF
For Binary: %
  b1010110 = %1010110
For Octal: Who cares?
  You won’t use it anyways.

## Slide 10: Flip-flops and Registers
Regardless of how you create it, a flip-flop stores precisely one bit of data.
  Lots of different styles: D, T, JK, SR
A register just plops a bunch of flip-flops together and usually provides simultaneous read/write capability.
Registers are the fundamental mode of data storage in processors.
  We’ll talk more about the memory hierarchy a little later.

## Slide 11: Buses
Buses are just parallel sets of wires, each carrying one bit of information, one part of the whole.
Most computers have multiple buses.

## Slide 12: Memory
Computer systems are nothing without memory.
Memory is usually organized as a square or rectangular array of cells, each capable of storing a single bit.
There are numerous data and control signals to access the memory.
These include:
  Read/Write
  Address Bus
  Data Bus
  Clock

## Slide 13: Memory Accesses
Despite data being stored in bits, memory is usually byte-addressable.
This means, you send in an address and get back one byte of data.
Reminder:
  Byte = 8 bits
  Nybble/Nibble = 4 bits
  Word = Some bits (In Motorola-land, it’s 8 bits)

## Slide 14: Endian-ness
Gulliver’s Travels, Jonathan Swift
  Lilliputians cracked their eggs on the little end -- hence Little Endians.
  Others cracked on the big end, the Big Endians.
  They fought a big, senseless war over it.
  I crack my egg in the middle.

## Slide 15: So What?
Processors are also Little and Big Endian.

## Slide 16: 16-bit Big vs. Little Endian
Writing the hex value $03E8

## Slide 17: 32-bit Big vs. Little Endian
Writing the hex value $12345678

## Slide 18: Endian-ness
Also may refer to the bit numbering.
  MSB on left with highest number is Big Endian
  MSB on right with lowest number is Little Endian
Most processors use Big Endian bit numbering
  Except Unisys and IBM

## Slide 19: My Experience
The Unisys cache wasn’t byte-addressable. We addressed 36-bit words.
When you asked for data from the 2nd Level Cache, you got back 8 words, the order of which depended on the actual word requested.
This word ordering was ridiculously complex.
It was also independently decided upon by the Processor and Cache guys.

## Slide 20: A Few Last Notes About Endian-ness
Bi-Endian
  Configurable to Little or Big
  PowerPC, MIPS, IA-64
Little Endian
  Intel x86 (IA-32), AMD64
Big Endian
  Sun Micro SPARC, Motorola 68000
Sometimes called “byte sex”
  In which case, bi-endian is called “bytesexual”
  Computer guys have a weird sense of humor

## Slide 21: Digital Computer Systems
Generically, a computer system includes some sort of storage and processing, along with support for various input and output devices.

## Slide 22: Digging Deeper
When we blow up the computer, we see four main components:
I/O Control
  Responsible for talking to the outside world
Main Memory
  A place to store stuff
The CPU
  Does the number crunching
Internal System Communication infrastructure

## Slide 23: One More Layer Down
Four basic subsystems within the processor:
Registers
  Close, fast storage for immediate values
ALU
  The part that actually does the number crunching
Control Unit
  Keeps thing running in an orderly fashion
Internal CPU Interconnects

## Slide 24: Let’s Think About Software
So you sit down to run a program.
It executes a line of code that was written in some high-level language like Java or C++ or whatever.
In reality, that line of code was compiled to some sort of intermediate form, then assembled to a machine code representation, which the computer executes, one instruction at a time.
An instruction is something very simple and atomic (e.g., AND, OR, XOR, load, store, etc.)

## Slide 25: Instruction Execution
There are generally three phases to every instruction’s execution:
  Fetch
  Decode
  Execute
We’ll go into greater detail on each of these phases later. For now, think of each phase as follows:

## Slide 26: Instruction Execution
Fetch (Get your orders)
  Go to memory to find out what your next task will be.
Decode (Read and understand the orders)
  Look at the contents of the instruction to find out what it is you are supposed to do, and find out if there’s more needed information.
Execute (Carry out the orders)
  Do it.

## Slide 27: So what is a Microcontroller?
A microprocessor is like the thing in your laptop, PDA, Dell or Macintosh. It just executes instructions.
A microcontroller also has on-board memory and I/O systems.
But so does a Pentium or Athlon or whatever.
In short, the line is blurry.

## Slide 28: Chapter 1 Summary
There are lots of different ways to represent binary numbers.
Registers are just a bunch of flip-flops.
Memory is just an array of places to store one bit of data, but is usually byte-addressable.
Computer systems are complex, but really contain a bunch of small, dedicated logic devices, connected together by a bus.
Fetch, decode, execute.
Microcontrollers are just microprocessors with on-board I/O and memory.