## Slide 1: EE 3170 Lecture 14
PIC16 Overview for the HC11-Savvy

## Slide 2: Topics
PIC 16 (Specifically, PIC16C77X)
I/O Systems
Memory Addressing
Interrupts
ISA
Stuff like that

## Slide 3: Getting to Know You
8 Characteristics to look at in any new microprocessor
  1. What does the pipeline look like?
  2. What is the register structure?
  3. What data types are supported?
  4. What unusual or “interesting” instructions exist?
  5. What is the subroutine call/return sequence like?
  6. What are its memory management conventions?
  7. How are exceptions and interrupts handled?
  8. How does it support co-processors?

## Slide 4: The PIC 16 Pipeline
Doesn’t exist.
The PIC is a RISC architecture, with regular classes of instructions, etc., but pipelines and real-time systems don’t always mix.
Microchip prides themselves on having provably secure and correct chips.
A pipelined PIC is not out of the realm of possibility.

## Slide 5: Execution Notes
Every instruction does only take 1 cycle
  Except:
    Taken branches
    Instructions that modify the PC
  These instructions are followed by a NOP, extending the duration of the instruction to 2 cycles.

## Slide 6: Getting to Know You
8 Characteristics to look at in any new microprocessor
  1. What does the pipeline look like?
  2. What is the register structure?
  3. What data types are supported?
  4. What unusual or “interesting” instructions exist?
  5. What is the subroutine call/return sequence like?
  6. What are its memory management conventions?
  7. How are exceptions and interrupts handled?
  8. How does it support co-processors?

## Slide 7: PIC Register Structure
Program Counter: 13 bits
General Purpose Registers:
  Don’t really exist as we know them
  4 “banks” of registers, with special purpose and general purpose mixed together.
  GP registers implemented as Static RAM
One “Working” register

## Slide 8: PIC Register File

## Slide 9: STATUS Register
PIC equivalent of the CCR

## Slide 10: More Register File
Looking back at the Register File diagram, there are a bunch of special purpose registers for control/status of I/O.
  What does this tell us about the type of I/O used?

## Slide 11: Getting to Know You
8 Characteristics to look at in any new microprocessor
  1. What does the pipeline look like?
  2. What is the register structure?
  3. What data types are supported?
  4. What unusual or “interesting” instructions exist?
  5. What is the subroutine call/return sequence like?
  6. What are its memory management conventions?
  7. How are exceptions and interrupts handled?
  8. How does it support co-processors?

## Slide 12: Supported Data Types
Not explicit.
The PIC16 is an 8-bit machine, so it supports all 8-bit data types
  Int, unsigned int, char
16-bit support would have to be through multiple instructions.
No floating/fixed point operations.

## Slide 13: Getting to Know You
8 Characteristics to look at in any new microprocessor
  1. What does the pipeline look like?
  2. What is the register structure?
  3. What data types are supported?
  4. What unusual or “interesting” instructions exist?
  5. What is the subroutine call/return sequence like?
  6. What are its memory management conventions?
  7. How are exceptions and interrupts handled?
  8. How does it support co-processors?

## Slide 14: Instruction Set Architecture
A whopping 35 instructions
  HC11: ~107
3 categories:
  Byte-oriented instructions
  Bit-oriented instructions
  Literal and Control instructions

## Slide 15: ISA Highlights
Not a lot of branches, just a GOTO instruction.
SLEEP instruction to enter stand-by mode.
Standard OR, AND, XOR instructions.

## Slide 16: Getting to Know You
8 Characteristics to look at in any new microprocessor
  1. What does the pipeline look like?
  2. What is the register structure?
  3. What data types are supported?
  4. What unusual or “interesting” instructions exist?
  5. What is the subroutine call/return sequence like?
  6. What are its memory management conventions?
  7. How are exceptions and interrupts handled?
  8. How does it support co-processors?

## Slide 17: Subroutines
To call a subroutine:
  call label
To return from a subroutine call:
  return

## Slide 18: Hardware Actions during Subroutine Calls
The PC is pushed to the stack.
  The stack is automatically initialized.
  But it’s only 8-deep.
  Subsequent interrupts or subroutine calls will obliterate the earlier return addresses.
  Only the lower 8 bits of the PC are accessible by code for manual storage of the PC.
On a return, the PC is popped off the stack.

## Slide 19: Getting to Know You
8 Characteristics to look at in any new microprocessor
  1. What does the pipeline look like?
  2. What is the register structure?
  3. What data types are supported?
  4. What unusual or “interesting” instructions exist?
  5. What is the subroutine call/return sequence like?
  6. What are its memory management conventions?
  7. How are exceptions and interrupts handled?
  8. How does it support co-processors?

## Slide 20: Memory Management
Program memory and data memory are logically (if not physically) separate.
Registers and memory are essentially the same thing.
Memory-mapped I/O in special-purpose register file (0x01-0x1F, 0x81-0x9F, non-contiguous)

## Slide 21: Port A
5/6 bit bi-directional port
Direction controlled by value of TRISA register.
Mulitplexed with Timer0 module.

## Slide 22: Port B
8-bits, bi-directional
Direction controlled by TRISB register
Multiplexed with:
  External Interrupt
  2 ADC Channels
Has “Interrupt on Change” capability

## Slide 23: Port C
8-bit, bi-directional
Direction controlled by TRISC register
Multiplexed with:
  SPI
  SSP
  I2C
  USART
  Timer0
  Timer1

## Slide 24: Port D
8-bit, input-only
TRISD register fixed as input
Not multiplexed with anything
Only on 40/44-pin devices

## Slide 25: Port E
3-bits, bi-directional
Direction controlled by TRISE register
  Also controls a bunch of other options for Port E
40/44-pin devices only

## Slide 26: Getting to Know You
8 Characteristics to look at in any new microprocessor
  1. What does the pipeline look like?
  2. What is the register structure?
  3. What data types are supported?
  4. What unusual or “interesting” instructions exist?
  5. What is the subroutine call/return sequence like?
  6. What are its memory management conventions?
  7. How are exceptions and interrupts handled?
  8. How does it support co-processors?

## Slide 27: Interrupts
One interrupt vector at 0x0004
Interrupts are globally enabled/disabled in the INTCON register.
INTCON also holds enables for the peripheral interrupts and timer interrupts.
PIE1 register holds the enables for specific peripherals.

## Slide 28: Hardware Actions on Interrupt
PC pushed to stack
I couldn’t find any info that interrupts were then disabled or not.
PC gets loaded with the interrupt vector.

## Slide 29: Software Actions on Interrupt
Poll the potential sources for the interrupt and service the appropriate one.

## Slide 30: Getting to Know You
8 Characteristics to look at in any new microprocessor
  1. What does the pipeline look like?
  2. What is the register structure?
  3. What data types are supported?
  4. What unusual or “interesting” instructions exist?
  5. What is the subroutine call/return sequence like?
  6. What are its memory management conventions?
  7. How are exceptions and interrupts handled?
  8. How does it support co-processors?

## Slide 31: Multi-/Co-processors
Minimal support through SPI.

## Slide 32: Various and Sundry
20 MHz Core clock
Direct, Indirect and Relative addressing modes
Power-On-Reset interrupt
Watchdog timer
3 Timers
Input Capture, Output Compare, PWM functions
12-bit multi-channel ADC
SSP, SPI, USART, I2C

## Slide 33: Development
Microchip offers many development programs, such as MPLAB, and at least 2 different C compilers.
Lots of other 3rd party solutions too

## Slide 34: Summary
Similar hardware capabilities, but the HC11 and PIC16 are radically different processors, reminiscent of two different development paradigms (CISC vs. RISC)
The PIC16 is a newer device, but may not necessarily be the better device.