## Slide 1: EE 3173 Lecture 7
Advanced Assembly Language Programming

## Slide 2: Lecture 7 Concepts
A Brief Programming Clinic
Advanced Programming Constructs
  if/then/else
  for loops
  while loops
  Declaring and using arrays
  Declaring and using strings

## Slide 3: Let’s Write a Simple Program
Think what you want to do.
  Consider flowcharting.
Determine what data you need.
  inputs
  outputs
Determine where to store the data.
  memory
  registers—Remember how few we have.
  stack

## Slide 4: Writing a Simple Program
Then think of what operations you need at the instruction level.
Write the sequence of instructions.
Check that they execute your desired operations.
Import your program to THRSim11 and verify.

## Slide 5: Programming Clinic
Write code to add 10 to the X register and subtract 100 from Y.
This problem is so simple we don’t need a flowchart.
The data are given as 10 and 100.
The registers are given as X and Y.
Thus the first thing we need to determine is which instructions to use.

## Slide 6: Programming Clinic
First we need an add.
  Choices are
    aba
    abx
    aby
    adca
    adcb
    adda
    addb
    addd

## Slide 7: Programming Clinic
We could also use increment in a loop
  inc
  inca
  incb
  ins
  inx
  iny
Not a great idea, really.

## Slide 8: Programming Clinic
So what do we do?
We would really like to add 10 to the X register but no instruction does that.
  There is no addx instruction and we can’t invent one.
  Our choices are between writing a loop to increment X 10 times or adding somewhere other than X.
  As X is a 16-bit register we must allow for 16-bit addition.
  The only 16-bit register for addition is D.
  Thus we choose addd.

## Slide 9: Programming Clinic
How do we get the number from X to D for addition?
  We might think of ldd with indexed X register addressing and an offset of 0.
    ldd 0,X
    but this doesn’t load D with the contents of X; it loads D from the memory location whose address is in X
  We could swap the X and D registers with the exchange instruction.
    xgdx

## Slide 10: Programming Clinic
Similar considerations apply to subtracting from Y.
  suba
  subb
  subd
For good practice we avoid the compare instructions which don’t put the difference anywhere accessible.

## Slide 11: Programming Clinic
Why don’t we use abx?
This adds the unsigned contents of B to X “considering the possible carry out of the low-order byte of X...”
  Do we know what this qualifier means?
    Do carries ripple across?
  It is limited to unsigned addition.
  It doesn’t affect the condition codes and hence can’t signal errors.
So we are better off using addd and knowing what we’re doing.

## Slide 12: Programming Clinic
What addressing mode do we use?
  We could use direct or extended.
    First we would have to put 10 and 100 in memory.
  Same for indexed.
  We can’t use inherent for 10 and 100.
  Relative makes no sense—used exclusively for branching relative to PC
  This leaves immediate.
    A great choice—just give value in second byte

## Slide 13: Programming Clinic
Our code
  xgdx ; Put X’s value in D for addition
  addd #10 ; Add 10
  xgdx ; Swap back, X has 10 more
  xgdy ; Now put Y’s value in D
  subd #100 ; Subtract 100
  xgdy ; Swap back, Y has 100 less

## Slide 14: Control Structures
Control structures are the basic building blocks of a program.
C control structures are
  if
  if-else
  while
  do-while
  for
  switch
We’ll do some of these in HC11 assembly language.

## Slide 15: if-then
Example: If M is less than or equal to N, complement M.
  ldx #M ldaa 0,X ldy #N cmpa 0,Y ; go to high if M > N bhi high ; complement M if M <= N coma high whatever

## Slide 16: if-then-else
We’ll extend it to if-then-else by adding an alternative action if the condition is false with an unconditional branch.
Example: If M <= N, complement M; otherwise decrement N.

## Slide 17: if-then-else, p. 2
  ldaa M cmpa N
  bhi high ; go to high if M > N
  coma ; complement M if M <= N
  bra merge
  high dec N
  merge whatever

## Slide 18: Switch Statements
Switch statements allow choosing among several paths.
  They are like Verilog case statements.
An expression is
  evaluated
  compared to several distinct values
  with a possible default
When the expression matches a value or default,
  actions are taken
  then control transfers to the end of the switch
The following partial example shows how we can set the steps for a stepper motor connected to PORT B, bits 3-0, in HC11 assembly language.

## Slide 19: Switch Example—Stepper Motor

## Slide 20: For Loops
“For” loops—as you know from HLL programming, are great for repetitive actions.
They’re also easy to implement in HC11 assembly language.
Consider the simple example on the next slide.

## Slide 21: We Need a Counter
A counter controls the number of times, N, the program goes through the for loop.
Initialize a counter before entering the for loop.
  0 for counting up to N
  N for counting down to 0

## Slide 22: For Loop Example
ldab #0 *initialize counter B
loop cmpb #100 *test for 100 times
bhs done *if done, continue
bsr/jsr
incb *increment counter
bra loop *do it again
done

## Slide 23: Arrays
Most real world applications require multiple chunks of related data.
Arrays are the logical choice to store them.
Most of the arrays we can easily deal with are static.

## Slide 24: Declaring an Array
Uninitialized
  array rmb 10
Initialized
  array fcb 1,2,3,4,5,6,7,8,9,10

## Slide 25: Accessing the Array
Load one of the index registers with the first address of the array, then use an indexed addressing instruction to access the data.
  org $0050 array rmb 10 ldx #array ldaa 8,X ; RegA = array[8] ldab #$19 stab 3,X ; array[3]= RegB
Array is zero-indexed.

## Slide 26: Iterating Through the Array
Use indexed addressing
Load the address of the first element of the array into an index register
At the end of the loop, increment the index register.
Load/store from 0,X or 0,Y

## Slide 27: Iteration Example
org $00F0 array rmb 10 ldx #array ldab #10 loop ldaa 0,X do_something; inx decb bne loop

## Slide 28: A Better Example
Eliminate “Magic Numbers”
arraySize equ 10 org $00F0 array rmb arraySize ldx #array ldab #arraySize loop ldaa 0,X do_something; inx decb bne loop

## Slide 29: Strings
In this class strings won’t be overly useful.
The lab projects use strings a lot.
The key thing to remember is that strings are just arrays full of ASCII characters.

## Slide 30: String Initialization
There is no “uninitialized” string allocation.
Using fcb
  myString fcb “Michigan Tech”
  But you need to set an option in THRSim to enable strings in the fcb directive!

## Slide 31: The Effect
Allocates 13 bytes of sequential memory
  4D 69 63 68 69 67 61 6E 20 54 65 63 68
  M i c h i g a n T e c h
The character delimiters are not included.
Check www.asciitable.com for full ASCII table.

## Slide 32: String Initialization
Using fcc
  myString fcc ‘Michigan Tech’
  myString fcc “Michigan Tech”
Both do exactly the same thing, which happens to be the same as an fcb.
But we don’t really like this. Instead, use:
  myString fcb “Michigan Tech”,0

## Slide 33: The Effect
14 bytes of sequential memory are allocated
  4D 69 63 68 69 67 61 6E 20 54 65 63 68 00
  M i c h i g a n T e c h \0
This is called a “null-terminated” string
  That character on the end is called the “null character”

## Slide 34: Which to Use?
Kind of a trick question
Always use a null-terminated string. It greatly simplifies the processing of the string.

## Slide 35: Processing a String
Canonicalize to upper-case
org $00F0 myString fcb “One World. Two wheels.”, 0 ldx #myString UpperCasify ldaa 0,X beq Done suba #$20 staa 0,X inx Done do_other_stuff;

## Slide 36: Examining Our String Processor
Why does this code work?
  Accesses characters in the string just like accessing characters in an array.
  The beq detects loading the null character.
The moral: If you don’t use a null-terminated string, you have to know the exact length of your string.

## Slide 37: Two-Dimensional Arrays
There is code in some books to deal with matrices (what normal programmers call two-dimensional arrays).
If you’re actually programming 2D arrays in assembly, you’ve lost your mind.

## Slide 38: A Subtle Difference
What is the difference between these two lines of code?
  myNumber fcb -12
  myNumber fcb “-12”

## Slide 39: Lecture 7 Summary
Some advanced programming constructs for smoothing out the transition from HLL to Assembly.
  If, if-then, switch, for loops
Arrays are good. Use indexed addressing to iterate through the array.
Strings are just arrays of characters.
  Always use a null-terminated string.