## Slide 1: EE 3173 Lecture 9
PCI Express

## Slide 2: Lecture 8 Concepts
PCI Express
  History
  How is it the same as “traditional” PCI?
  How is it different than “traditional” PCI?
  How does it work in general?
    Transactions, bus synchronization, bus arbitration, etc.

## Slide 3: PCI Express
By April 2002, the PCI-SIG and Arapahoe Work Group finished the 3GIO draft specification, formally renaming it "PCI Express".
A Point-to-point bus interface under development by the PCI SIG
Bidirectional sequential serial interconnect
Higher quality of service, bandwidth
Co-exists w/ PCI
PCI Express – inside chassis
Infiniband - Outside chassis

## Slide 4: PCI SIG Goals
Supports multiple market segments and emerging applications
  Unifying I/O Architecture for Desktop, Mobile, Server, Communications Platforms, Workstations and Embedded Devices.
Low cost and high volume
  Cost at or below PCI cost structure at the system level
PCI Compatible software model
  Boot existing operating systems without any change. PCI compatible configuration and device driver interfaces.
Performance
  Scalable performance via frequency and additional lanes. High Bandwidth per Pin. Low overhead. Low latency.
Support multiple platform connection types:
  Chip-to-chip, board-to-board via connector, docking station and enable new form factors.
Advanced features
  Comprehend different data types. Power Management. Quality Of Service. Hot Plug and Hot Swap support. Data Integrity and Error Handling. Extensible. Base mechanisms to enable Embedded and Communications applications.

## Slide 5: PCI Express Design motivations
AGP was NOT very scalable
  Architected for a single graphics slot
  Scaled frequency over the bus life-cycle
PCI Express planned for scalability
  Scalable bus widths : x1, x2, x4, x8, x16
    Port Splitting
    Down-shifting
  Frequency scaling: 2.5GHz (Gen1), 5GHz (Gen2)
  General purpose bus means multiple slots available for scaling performance
    SLI – multiple graphics cards

## Slide 6: PCI Express

## Slide 7: Slot Form
Slots can co-exist on the same board
Not compatible with any other form
Not using the same case slot (ISA / PCI)

## Slide 8: PCI Express Mechanical

## Slide 9: PCI Express Connector Pinout
Extensible
Large Fraction of pins for Ground
Differential Signaling

## Slide 10: Conventional PCI on the Desktop
PCI NIC card...
...and today’s PCI-Based Motherboard

## Slide 11: PCI Express on the Desktop
PCI-E X1 NIC card
And a motherboard with PCI and PCI-E slots... is expected to save board space and enable smaller form factors

## Slide 12: PCI Express: Removing the Bottlenecks
32-bit PCI Architecture provides 133 MB/sec. shared bandwidth
PCI bandwidth has not scaled
  High performance 64-bit architectures limited to high-end systems

## Slide 13: PCI Express Architecture
PCI Express is a highly scaleable serial bus architecture that will eventually replace today’s PCI & AGP busses
PCI Express devices will use a variety of “lanes” to scale
  Each “lane” is two bits wide (one in each direction) & can provide 5Gb/sec bandwidth
  PCI Express will be found in x1, x4, x8, and x16 configurations
PCI Express x1
PCI card replacement; Typical x1 devices will be Network cards, Modems, etc
PCI-E x1 bandwidth designed to provide 500MB/sec. vs. 133MB/sec for 32-bit/33 MHz PCI
Device A
Device B
PCI Express x4 & x8
Used for high-end networking & storage solutions such as dual GbE, 10GbE & SANs
PCI-E x4/x8 support will be limited to enterprise & workstation systems
Device A
Device B
PCI Express x16
The AGP replacement
The AGP bus tops out at 2 GB/sec. bandwidth (AGP 8x) while PCI-E x16 is designed to provide 8GB/sec. of bandwidth
Device A
Device B
www.usit.uio.no/it/lita/itkonferanse-2004/ foiler/UIO_Seminar_dell.ppt
Notes: PCI Express is a highly scaleable serial bus architecture that will replace today’s PCI & AGP busses
  Don’t confuse PCI Express with PCI-X, which is a high bandwidth variant of today’s parallel PCI architecture
PCI Express uses selectable “lane” architecture to scale
  Each “lane” is two bits wide (one in each direction) - - - Each PCI-E lane is designed to provide 5 Gigabits per second bandwidth - - - PCI Express is designed to enable performance increases over time
  The PCI-E lane architecture is designed such that a x1 card can be used in a x16 slot - - - NO MORE DEDICATED SLOTS, PROVIDING YOU GREATER FLEXIBILITY
PCI Express will initially be found in x1, x4, x8, and x16 configurations
  x1 is like today’s PCI, except with a lot more bandwidth for the future
  x4 and x8 are for high bandwidth apps, like high-end storage and communications
  x16 is for graphics, and is expected to provide 5 times the bandwidth of AGP 8x
Due to the reduced pin count of PCI Express, PCI E is predicted to be a cost effective way to deliver high bandwidth for the future for both desktops & notebooks
OptiPlex 280 series chassis’ will have:
SMT – 3 PCI and 1 PCI-E x1 and 1 PCI-E x16
SD – 1 PCI-E x16 (low profile) and a riser with 2 PCI slots on the riser FULL HEIGHT. Via CFI customers can get and optional riser (1 PCI-E x1 and 1 PCI) in lieu of the factory installed riser.
SFF – 1 low profile PCI slot and 1 PCI-E x16 (low profile)
UFF – no slots

## Slide 14: Virtual Channels
http://www.pcisig.com/specifications/pciexpress/technical_library/dev_con_09_02/specifications/pciexpress/PCIExpress_ArchOverview.pdf

## Slide 15: Use of Multiple Lanes
http://www.pcisig.com/specifications/pciexpress/technical_library/dev_con_09_02/specifications/pciexpress/PCIExpress_ArchOverview.pdf

## Slide 16: Layered Protocols
http://www.pcisig.com/specifications/pciexpress/technical_library/dev_con_09_02/specifications/pciexpress/PCIExpress_ArchOverview.pdf

## Slide 17: Packet Formation
http://www.pcisig.com/specifications/pciexpress/technical_library/dev_con_09_02/specifications/pciexpress/PCIExpress_ArchOverview.pdf

## Slide 18: Creating Transactions
The Software Layers create a request which the Transaction Layer turns into a packet.
The Link Layer adds sequence information and CRC (Cyclic Redundancy Check) to the packet.
The physical layer is manifested as two twisted-pairs, one for transmittal and one for reception.

## Slide 19: Transaction Protocol
http://www.pcisig.com/specifications/pciexpress/technical_library/dev_con_09_02/specifications/pciexpress/PCIExpress_ArchOverview.pdf

## Slide 20: Packet Headers
http://www.pcisig.com/specifications/pciexpress/technical_library/dev_con_09_02/specifications/pciexpress/PCIExpress_ArchOverview.pdf

## Slide 21: Signalling
http://www.pcisig.com/specifications/pciexpress/technical_library/dev_con_09_02/specifications/pciexpress/PCIExpress_ArchOverview.pdf

## Slide 22: Embedded Clocking
http://www.pcisig.com/specifications/pciexpress/technical_library/dev_con_09_02/specifications/pciexpress/PCIExpress_ArchOverview.pdf

## Slide 23: Comparing PCI and PCI-Express
What’s the same?
  The software interface
  Still synchronous, though PCI-E clock is embedded into transmission via 8b/10b encoding.
What’s different?
  Pretty much everything else.
  From parallel multi-drop bus to serial point-to-point protocol.
  No arbitration.
  Much higher data transfer rates
  Variable connection widths.

## Slide 24: Intel’s Comparison

## Slide 25: Low-Voltage Differential Signaling (LVDS)
Definition: LVDS uses high-speed analog circuit techniques to provide multigigabit data transfers on copper interconnects.
  A generic interface standard for high-speed data transmission.
The American National Standards Institute (ANSI)/Telecommunications Industry Association (TIA)/Electronic Industries Alliance (EIA) 644-1995 standard specifies the physical layer as an electronic interface.
This standard defines driver and receiver electrical characteristics only. It does not define protocol, interconnect, or connector details because these details are application-specific.

## Slide 26: The Bad Old Days
Consider RS-232: voltage swings of as much as 24 volts.
  Takes a lot of time!
We’ve tried lots of things like LVTTL (Low-Voltage Transistor-to-Transistor Logic), Gunning Transistor Logic (GTL) and Stub Series Terminated Logic (SSTL) to reduce power.
LVDS reduces it even further.

## Slide 27: What is Differential Signaling?
First, consider a seesaw: as one person goes up, the other goes down, but their average position remains the same. More importantly, their relative position remains the same.
A positive value may be represented by the left person being higher than the one on the right, while a negative value is represented by the right person being higher. Zero is represented when the two people are level with each other.
http://www.latticesemi.com/lit/docs/appnotes/pac/an6019.pdf?jsessionid=ba30ce0b2130$3F$3F$0

## Slide 28: Off the Playground
Real Differential Signaling looks like this:

## Slide 29: Differential Signaling
Differential signaling uses two conductors
  The transmitter translates the single input signal into a pair of outputs that are driven 180° out of phase.
  The receiver, a differential (or subtracting) amplifier, recovers the signal as the difference in the voltages on the two lines.
Advantages of differential signaling can be summed up as follows
  Differential Signaling is not sensitive to most noise.
  A differential receiver is tolerant of its ground moving around.
  If each “wire” of pair is on close proximity of one and other. electromagnetic interference imposes the same voltage on both signals. The difference cancels out the effect.
  Since the AC currents in the “wires” are equal but opposite and proximal, radiated EMI is reduced.

## Slide 30: What LVDS Gives Us
Differential signals are immune to common-mode noise.
A voltage change between logic states of only 300 mV
  So LVDS can change states very fast.
An LVDS signal also changes voltage levels without a fast slew rate.
  The slew rate refers to how fast an amplifier reacts to changes in inputs. Normally, a higher slew rate is better.
For LVDS, however, slower transitions reduce the problem of reflections from transmission-path impedance discontinuities, decreasing emissions and crosstalk problems.
Low-voltage swing reduces power consumption because it lowers the voltage across the termination resistors and lowers the overall power dissipation.
Intel claims that PCI-E (and others) really use Current Mode Logic, but the basic point remains.

## Slide 31: PCI 2.0
2.0 specification doubles the interconnect bit rate from 2.5 Gbs to 5 Gbs.
  16-lane link bandwidth to approximately 16 GB/s
Dynamic link speed management to control the speed at which the link is operating
Link bandwidth notification to notify software (operating system, device drivers, etc) of changes in link speed and width
Capability structure expansion to expand the control registers to better manage devices, slots and the interconnect
Access control services optional controls to manage peer-peer transactions
Completion timeout control to define a required disable mechanism plus related optional enhancements
Function-level reset, an optional mechanism to reset functions within a device
Power limit redefinition to redefine slot power limit values to accommodate devices that consume higher power

## Slide 32: PCI-E 2.0 Devices Available
NVIDIA nForce 750i SLI Motherboard
  Available at Amazon since January 17, 2008.
NVIDIA GeForce 8800
  First PCI 2.0 video card, available since October 2007
AMD 7-Series Chipsets
  Supports 42 PCI-E 2.0 lanes
And probably lots more.

## Slide 33: PCI X.0?
Atomic Memory Operations
  Fetch-and-Add, Swap, Compare-and-Swap
Multicast
  Non-trivial for a point-to-point protocol!
Internal Error Reporting
  Just for PCI-E protocol things
Opaque Transaction Hint
  Here’s how you can optimize this data when you get it.
Dynamic Power Allocation
  Don’t need the power? Fine. I won’t send it.

## Slide 34: Lecture 9 Summary
PCI Express is a great example of the transition from parallel to to high-speed serial busses.
There’s very little in common between PCI and PCI Express.
LVDS is a big deal.
  Remember, P = V2/R.