## Slide 1: EE 3173 Lecture 14
CAN - The Controller Area Network

## Slide 2: Lecture 12
CAN: The Controller Area Network
History, Development, Motivation
Transactions
  Format
  Commands
  Error Detection

## Slide 3: Development
So BMW and Mercedes engineers were sitting around one day complaining about how all the processors in their cars wouldn’t talk each other’s language.
They went to engineers at Robert Bosch GmbH, and Bosch developed CAN.
  GmbH = Gesellschaft mit beschränkter Haftung, or basically “Limited Liability Corporation”.
Developed back in mid-1986.
By 1987 Intel had CAN silicon.

## Slide 4: The Point
CAN is a serial communications protocol which efficiently supports distributed real-time control with a very high level of security.
Its domain of application ranges from high speed networks to low cost multiplex wiring.
  Automotive electronics, engine control units, sensors, anti-skid-systems, etc.
Bit rates up to 1 Mbit/s
At the same time it is cost effective to build into vehicle body electronics.

## Slide 5: CAN Priorities
Prioritization of messages
Guarantee of latency times
Configuration flexibility
Multicast reception with time synchronization
System wide data consistency
Multimaster
Error detection and signaling
Automatic retransmission of corrupted messages as soon as the bus is idle again
Distinction between temporary errors and permanent failures of nodes and autonomous switching off of defect nodes

## Slide 6: Yet Another Layered Protocol
Three Layers
  Object Layer
  Transfer Layer
  Physical Layer
As far as we are really concerned, only the Transfer Layer is really important.
The other two are summarized on the next slide.

## Slide 7: Object Layer and Physical Layer
The Object Layer:
  Finds messages are to be transmitted
  Decides which messages received by the transfer layer are actually to be used
  Provides an interface to the application layer related hardware.
  Thus sayeth the spec: “There is much freedom in defining object handling.”
The Physical Layer:
  Whatever works for you, but it had better be pretty noise tolerant.
  Tends to be differential pairs. Twisted pair is even better.

## Slide 8: Some Transfer Layer Basics
Messages: The basic unit of transfer. Various sizes, contents and priorities.
CSMA/CD Network
A CAN Node knows nothing about the network it is on.
  But that’s okay!
  In fact, it’s pretty useful. It leads to the following desirable characteristics for CAN…

## Slide 9: I know nah-sink!
Benefits of “Network Ignorance”
  System Flexibility
    No handshaking, introductions, etc.
    No limitation to number of devices.
  Message Routing
    The Message ID doesn’t indicate who it’s from or who it’s to, but what it means! Each node decides whether it needs to act upon that message.
  Multicast
    Every node can receive a message.
  Data Consistency
    Everybody should see the same message.

## Slide 10: Some More Basics
The bit rate of CAN is flexible, but is always fixed within a given system.
Multimaster
  There is no specific bus master. Any node may begin transmitting anytime the bus is free.
Arbitration
  Not based on device priority, but message priority!
  A system of dominant and recessive bits determines if what a unit is currently sending is more or less important that whatever else might be transmitting concurrently.

## Slide 11: Ensuring Data Integrity
Data “safety” is paramount.
For detecting errors the following measures have been taken:
  Monitoring
    (Transmitters compare the bit levels to be transmitted with the bit levels detected on the bus)
  Cyclic Redundancy Check
  Bit Stuffing
    Inserting a transition after a maximum number of sequential identical values
  Message Frame Check

## Slide 12: Does It Work?
All global errors are detected.
All local errors at transmitters are detected.
Up to 5 randomly distributed errors in a message are detected.
Burst errors of length less than 15 in a message are detected.
Errors of any odd number in a message are detected.
Total residual error probability for undetected corrupted messages:
  < (message error rate) * 4.7 x 10-11.

## Slide 13: Even More Basics
Any node detecting an error can flag it, even if it doesn’t particularly care about the message.
  Recovery period is no more than 29 “bit times”.
The bus can have one of two complementary logical values: dominant or recessive.
During simultaneous transmission of dominant and recessive bits, the resulting bus value will be dominant.
  For example, in case of a wired-AND implementation of the bus, the dominant level would be represented by a logical 0 and the recessive level by a logical 1.

## Slide 14: Last Basic Things
Acknowledgment
  All receivers check the consistency of the message being received and will acknowledge a consistent message and flag an inconsistent message.
Sleep Mode / Wake-up
  To reduce the system’s power consumption, a CAN-device may be set into sleep mode without any internal activity and with disconnected bus drivers.
  The sleep mode is finished with a wake-up by any bus activity or by internal conditions of the system.
  On wake-up, the internal activity is restarted, although the transfer layer will be waiting for the system’s oscillator to stabilize and it will then wait until it has synchronized itself to the bus activity before the bus drivers are set to "on-bus" again.
  In order to wake up other nodes of the system, which are in sleep-mode, a special wake-up message with the dedicated, lowest possible IDENTIFIER is used.

## Slide 15: Frames
A data frame carries data from a transmitter to the receivers.
A remote frame requests transmission of the data frame with the same identifier.
An error frame is transmitted by any unit on detecting a bus error.
An overload frame is used to provide for an extra delay between the preceding and the succeeding data or remote frames.

## Slide 16: Data Frame Fields
Start of Frame
  Marks the beginning of data frames and remote frames. It consists of a single dominant bit.
  A station is only allowed to start transmission when the bus is idle.
  All stations have to synchronize to the leading edge caused by start of frame of the station starting transmission first.
Arbitration Field
  Consists of the identifier and the RTR Bit.
  Identifier
    11 bits wide, ID10..ID0.
    The 7 most significant bits must not be all recessive.
  RTR Bit
    Remote Transmission Request Bit
    Data Frame: Dominant
    Remote Frame: Recessive

## Slide 17: More Data Frame Fields
Control Field
  6 bits wide
  Include the data length code and two bits reserved for future expansion
  The reserved bits have to be sent dominant.
Data Length Code
  The number of bytes in the data field is indicated by the data length code.
  Obviously means a data frame can only contain 8 bytes of data.
  Wait, what?

## Slide 18: That Data Length Code Thing
The msb doesn’t really get used, except for 8-byte transfers.
I don’t know. “By all accounts, it doesn't make sense.”

## Slide 19: More Data Frame Fields
Data Field
  Contains from 0 to 8 bytes, which each contain 8 bits which are transferred MSB first.
CRC Field
  Contains the CRC sequence followed by a CRC delimiter.
CRC Sequence
  The frame check sequence is derived from a cyclic redundancy code best suited for frames with bit counts less than 127 bits.
CRC Delimiter
  A single recessive bit.

## Slide 20: More Data Frame Fields
ACK Field
  Two bits long
  Contains the ACK Slot and the ACK Delimiter.
  In the ACK FIELD the transmitting station sends two recessive bits.
  A receiver which has received a valid message correctly, reports this to the transmitter by sending a dominant bit in the ACK Slot.
  The ACK Delimiter is always a single recessive bit.
End Of Frame
  7 recessive bits

## Slide 21: Remote Frames
Looks pretty much like a data frame, except the RTR bit is recessive and there’s no data.

## Slide 22: Error Frames

## Slide 23: Error Frames
The Error Flag is one of two types:
  Passive or Active
An Active Error flag is six consecutive dominant bits.
  This violates bit stuffing rules, and causes everybody else to cry foul too.
  Will only be generated by an actively error checking station.
Passive error flags are six consecutive recessive bits.
  Only generated by passive stations.
  Could be overwritten or ignored by other devices.
ERROR Delimiter
  Eight recessive bits.
  After an Error Flag each station sends a recessive bit and monitors the bus until it detects a recessive bit. Then, it sends seven more recessives.

## Slide 24: Uh-oh. Something’s wrong.
Five Error Conditions
  Bit Error: When the bit value that is monitored is different from the bit value that is sent.
    An exception is the sending of a recessive bit during the stuffed bit stream of the Arbitration Field or during the ACK Slot.
  Stuff Error: When the 6th consecutive equal bit level in a message field that should be “stuffed”.
  CRC Error: If the calculated result is not the same as that received in the CRC sequence.
  Form Error: When a fixed-form bit field contains one or more illegal bits.
  Acknowledgment Error: When a transmitter does not monitor a dominant bit during the ACK Slot.

## Slide 25: What do we do about these errors?
CAN claims to be a fault-tolerant bus.
How does it live out this claim?
One of the biggest questions: What does it do about a “babbling idiot’?

## Slide 26: CAN Fault Confinement
Every busy unit maintains two counts:
  Receive Error Count
  Transmit Error Count
A series of rules modifies these counts.
  If Receive Error Count or Transmit Error Count >= 127, a unit is forced into “passive error” mode.
  You get kicked off the bus if Transmit Error Count >= 256.
These counts seem large. 256 errors? Let’s take a look at the rules.

## Slide 27: Fault Count Rules
1. When a receiver detects an error, the Receive Error Count will be increased by 1, except when the detected error was a Bit Error during the sending of an Active Error Flag or an Overload Flag.
2. When a Receiver detects a dominant bit as the first bit after sending an error flag, the Receive Error Count will be increased by 8.
3. When a Transmitter sends an error flag, the Transmit Error Count is increased by 8.

## Slide 28: More Error Counting
4. If an Transmitter detects a bit error while sending an Active Error Flag or an Overload Flag the Transmit Error Count is increased by 8.
5. If an Receiver detects a Bit Error while sending an Active Error Flag or an Overload Flag the Receive Error Count is increased by 8.
6. Any node tolerates up to 7 consecutive dominant bits after sending an Active Error Flag, Passive Error Flag or Overload Flag. After detecting the 14th consecutive dominant bit (in case of an Active Error Flag or an Overload Flag) or after detecting the 8th consecutive dominant bit following a Passive Error Flag, and after each sequence of additional eight consecutive dominant bits every Transmitter increases its Transmit Error Count by 8 and every Receiver increases its Receive Error Count by 8.

## Slide 29: More Error Counting
After the successful transmission of a message (getting ACK and no error until End of Frame is finished) the Transmit Error Count is decreased by 1 unless it was already 0.
8. After the successful reception of a message (reception without error up to the ACK Slot and the successful sending of the ACK bit), the Receive Error Count is decreased by 1, if it was between 1 and 127. If the Receive Error Count was 0, it stays 0, and if it was greater than 127, then it will be set to a value between 119 and 127.

## Slide 30: Some Notes on Errors
“An error count value greater than about 96 indicates a heavily disturbed bus. It may be of advantage to provide means to test for this condition.”
  96/8 = 12
Errors before a node goes passive:
  128/8 = 16
Errors before a node gets kicked off:
  256/8 = 32

## Slide 31: So What About the Babbling Idiot?
CAN doesn’t provide any particular support for detection and elimination of babbling idiots.
Other competitive protocols such as TTP (Time Triggered Protocol) find this to be a distinct shortcoming of CAN.