## Slide 1: EE 3173 Lecture 10
SCSI

## Slide 2: Lecture 10 Concepts
SCSI History, Development and Purpose
SCSI Terms and Functions
SCSI Command Execution
SCSI Hardware
The Future of SCSI

## Slide 3: Credits
Much of this slideset comes from the booklet Basics of SCSI, 4th Edition, written by Jan Dedek. Published by Ancot Corporation.

## Slide 4: Intro to SCSI
A Parallel Data Bus -- Small Computer Systems Interface
  History dates back to the Selector Channel on IBM-360 mainframes.
  Scaled down by Shugart Associates in the late 70’s to a disk drive interface and named “Shugart Associates Systems Interface” or SASI (pronounced “sassy”).
  SA pushed for standardization and after 4+ years in committee, SCSI was born.
  Standardized by ANSI.
  Occasionally referred to as SC/ASI in older documents.

## Slide 5: SCSI Standards
Many interfaces
  Fast SCSI, Fast Wide SCSI, Ultra SCSI, Ultra Wide SCSI
Only three standards
  Creatively named SCSI-1, SCSI-2, SCSI-3
  Maintained by the SCSITA
But the standards are really just loose suggestions. A manufacturer gets to pick and choose which parts of the standard a device complies to.

## Slide 6: SCSI-1
8-bit parallel bus (with parity)
  Called Narrow SCSI
Running asynchronously at 3.5 MB/s or 5 MB/s in synchronous mode
Maximum bus cable length of 6 meters
Bus clock was 5 MHz
Maximum of 7 devices (excluding HBA)
  Why not 28?

## Slide 7: Synchronicity
Asynchronous transfers require each byte to be requested and acknowledged before the next one comes along.
  Generally used to “slow down” a fast device when communicating with a slower one.
Synchronous transfers allow data to come out as fast as the bus allows, provided the transmitter respects the queue depth of the receiver.
Synchronous mode is only for data. Commands are still asynchronous.
Communication with other devices on the bus may be mixed between synchronous and asynchronous.
Synchronicity is negotiated between the two devices.

## Slide 8: SCSI-2
Where it all begins to fall apart.
Fast SCSI -- Any transfer rate above 5 MHz. Usually designated Fast/10.
  Obviously, Fast/10 had a 10 MHz clock
Wide SCSI doubled the data path to 16 bits.
  Also supports 15 devices (excluding HBA).
So we have Fast SCSI, Fast Wide SCSI, and vanilla SCSI.
Cable length dropped to 3 m.
  Bummer.

## Slide 9: SCSI-3
Last of the dinosaurs.
Added a Fast/20, usually called Ultra.
So now we have SCSI, Fast SCSI, Fast Wide SCSI, Ultra SCSI and Ultra Wide SCSI.
Cable length still just 3 m.
Ultra SCSI had some serious reliability issues, mainly noise and interference sensitivity.
No SCSI-4, because the interface was disassociated from the protocol at this point. The command set has remained constant, but we’ve seen a huge number of physical interfaces.

## Slide 10: Further SCSI Interfaces
Ultra-2 SCSI
  80 MB/s transfer, LVD signalling.
  Max cable length extended to 12 m, largely thanks to the LVD.
  Didn’t last long.
Ultra-3 SCSI
  Upped transfer rate to 160 MB/s using DDR
  Offered CRC instead of just parity.
Ultra-320 SCSI
  Data rate increased to 320 MB/s
  If you have a modern parallel SCSI device, it’s probably an Ultra-320 device.

## Slide 11: The Newest SCSI Interfaces
Ultra-640
  Pretty much ignored, since cable lengths restricted the number of devices on the bus to about 1 or 2.
Serial SCSI
  Numerous standards have appeared that map the SCSI command set onto a serial transmission protocol including:
    Serial Storage Architecture (SSA), Fibre Channel Arbitrated Loop (FC-AL), FireWire and Serial Attached SCSI (SAS).
    In 1999, I worked at IBM on their FC-AL drives, and we were the black sheep.

## Slide 12: Connectors
Oddly enough, the SCSI standard has never described what the connector looks like. Most parallel SCSI connectors ended up looking like this though:

## Slide 13: Terminology
Host Bus Adapter: A translator from SCSI to PCI/EISA/whatever at the computer host.
Initiator: Almost always the host adapter. Kicks off the transfer.
Target: Almost always a peripheral. Responds to the transfer.
Peripherals may need to act as Initiators, BAs may need to act as Targets.
There always must be one Initiator and one Target on a fully functional SCSI bus.

## Slide 14: Device Addressing
Each device has a SCSI ID that is 1 bit.
  Set via jumpers or software.
IDs are not encoded, so an 8-bit bus only allows for 8 total devices, one of which must be the HBA.
A device may have up to 8 Logical Units, each with a Logical Unit Number or LUN.
  The logical unit concept is as flexible as the rest of the standard.
The higher the SCSI ID, the higher the priority on the bus.
  The HBA is normally 7.

## Slide 15: Disconnect - Reconnect
Fancy SCSI terms for split-transactions. A long operation may cause the target to disconnect from the bus so that other devices may do their thing.
When the operation is complete, the target reconnects, does the data transfer and terminates.

## Slide 16: Logical Blocks
SCSI was primarily for storage, and when addressing a storage device, data storage locations were presented to the system as Logical Blocks, each with a Logical Block Address (LBA).
The max LBA is determined by a SCSI command called Read Capacity.
The LBA shows up a lot in any given SCSI read/write commands.

## Slide 17: SCSI Device Types
SCSI-1 defined 5 device classes:
  1 - Random Access 2 - Sequential Access 3 - Printer 4 - Processor 5 - Write Once device 6 - Read Only random access
SCSI-2 Defined 4 additional classes:
  6 - CD-ROM (Replaced the old #6) 7 - Scanner 8 - Magneto Optical 9 - Medium Changer (Jukebox) 10 - Communication

## Slide 18: SCSI-3 Device Types
SCSI-3 Redefined all of these:
  1 - Block Device (Magnetic & Optical Disks) 2 - Stream Devices (Tapes, Processors) 3 - Graphic Devices (Printers, Scanners) 4 - Medium Changers (Jukeboxes) 5 - RAID Controllers 6 - CD-ROMs 7 - Enclosures (Environmental Services)

## Slide 19: SCSI Commands
A command comes into a device in a CDB (Command Descriptor Block).
The size of the CDB varies, but this basic format holds:
  Byte 1: Op Code
  Byte 2: LUN (Upper 3 bits only) and LBA
  Bytes 3-5/9/11: LBA and transfer length
  Byte 6/10/12: Control Byte

## Slide 20: Command Phases
A Comprehensive list is:
  Arbitration Selection Message Out Message In Command Data Out Data In Status Bus Free
The usual sequence of events is:
  Arbitration Selection Message Out Command Data In/Out Status Message In

## Slide 21: Command Linking/Queuing
In the Control Byte of the CDB is the Link bit. Multiple commands can be linked together so that an operation is not interrupted by another initiator.
Command Queuing is when a device holds on to incoming commands and executes them in an optimal order. Another optional functionality.

## Slide 22: SCSI Bus Signals
BSY: Wired-OR that indicates bus activity
SEL: Wired-OR that selects a target (or re-selects an initiator)
Control/Dat, In/Out, MSG: Driven by Target to move though various phases of the bus
REQ: Data strobe driven by the Target
ACK: Data strobe driven by Initiator in response to an REQ
ATN: Driven by Initiator to indicate it has a message for the Target
RST: Bus Reset line
DATA: Umm, data?
PARITY: Odd parity for the data
DIFFSENSE: Indicates whether the interface is HVD or LVD.

## Slide 23: Bus Arbitration
Independent Request
When a device wants the bus, it asserts the BSY line and the bit on the data lines associated with its SCSI ID.
The highest priority device gets the bus, then begins the Selection phase.
Other devices that lost back off.
The target’s ID is asserted on the data lines and the SEL line is asserted.
When the target notices, it drives the BSY line and the transaction proceeds.

## Slide 24: Data Transfer
If the ATN line is driven during the Selection phase, there is a Message Out phase where the target LUN of the target device is presented on the data bus.
  Optional in SCSI-1, mandatory in SCSI-2.
Command phase comes next, where the CDB is transmitted to the Target.
Data is actually transfer in the Data-In or Data-Out phases, depending on the nature of the transfer.

## Slide 25: Completing the Transfer
A Status phase then follows where command completion status is reported to the Initiator.
The command is completed with a Message-In phase where the message is (hopefully) simply “Command Complete.”

## Slide 26: Example Write Command
Bus Free Arbitration /80 (7) Select w/ATN /81 (0,7) Message-Out /C0 (Identify: LUN0 Disconnect OK) Command /0A 00 00 00 01 00 (Write) Data-Out /00 00 00 00…… Message-In /04 (Disconnect) Bus Free Arbitration /01 (0) Reselection /81 (0,7) Status /00 (Good) Message-In /00 (Command Complete) Bus Free

## Slide 27: What Just Happened?
The Initiator (device 7) arbitrated for the bus and won.
It selected device 0 and LUN 0 and indicated that disconnects were acceptable.
The target saw that and was cool with it.
The write command came across.
Then a bunch of data (not really shown).
The target sent a message of 0x04, indicating a disconnect.
Eventually, device 0 arbitrated for the bus so it could indicate transfer completion to the initiator with a Reselection, a Good status and a Command Complete.
What this indicates is that the target has a buffer of some sort, so it immediately took the data, let other devices use the bus while it was busy, and then indicated completion.

## Slide 28: An Example Read
Bus Free Arbitration /80 (7) Select w/ATN /81 (0,7) Message-Out /C0 (Identify: LUN 0 Disconnect OK) Command /08 00 00 10 20 00 (Read) Message-In /04 (Disconnect) Bus Free Arbitration /01 (0) Reselection /81 (0,7) Message-In /80 (Identify: LUN 0) Data-In /00 00 00… Status /00 (Good) Message-In /00 (Command Complete) Bus Free

## Slide 29: That Read Operation in English
Device 7 arbitrated and won.
Selected Device 0, LUN 0 and indicated disconnecting was okey-dokey.
Issued the Read command.
Device 0 said, “Aye-aye sir,” and disconnected to go get that data.
When the data was ready, the target arbitrated, won and reconnected to the initiator.
It then sent the data, a Good status message and a Command Complete message.

## Slide 30: SCSI’s Future
As far as most people are concerned, the future of SCSI is serial. Most eggs are in one of two baskets: SAS or FC-AL.
Fibre Channel seems to be doing better, even though the SCSITA prefers SAS.
  Seagate sells 20 different FC-AL drives, but 14 SAS drives (and >40 parallel SCSI drives).
  Hitachi GST sells their UltraStar server-class drives in U320 SCSI, SAS, and 2 different flavors of FC, pretty much equal-opportunity.
There’s also an iSCSI that operates over a standard TCP/IP connection.
SCSI has always been a server-oriented protocol, and will continue to be, especially with PCI Express and SATA out.

## Slide 31: Lecture 10 Summary
SCSI was designed for storage.
It’s a loose standard, and has a lot of physical implementations.
As a parallel standard, it’s almost entirely dead.
As a serial standard, it’s flourishing still.