## Slide 1: EE 3173 Lecture 6
Transmission Error Prevention, Detection and Correction

## Slide 2: Concepts for Lecture 6
Error Prevention
  Bit Stuffing
Error Detection
  Parity
  CRC
Error Correction
  Hamming Codes

## Slide 3: Bit Stuffing
The basic concept here is to limit the number of sequential 1’s.
Protecting against a “stuck-at” fault.
Generally forbid more than 5 sequential 1’s in a row, at which point a 0 is forcefully inserted by the transmitter.
The receiver must undo this stuffing in order to receive correct data.
Application: CAN

## Slide 4: Bit Stuffing Example
Consider the data packet 0111 1111 0000
  We have 7 ones in a row, which, if sent, would violate our rules.
  So we send: 0111 1101 1000 0
  The overhead isn’t too bad.

## Slide 5: Error Detection: Parity
Single-bit error detection
An agreement between the transmitter and receiver as to how many 1’s will be transmitted in a data packet.
Choices are even and odd.
Two problems with parity:
  1. Which bit had the error? We don’t know.
  2. What happens when two bits flip? 3? 4?

## Slide 6: Example: Calculating Parity
Even parity:
  Data packet = b10110110
  Parity Bit = b1
  Total of 6 1’s
Odd parity:
  Data packet = b10110110
  Parity Bit = b0
  Total of 5 1’s

## Slide 7: Example: Parity Errors
Data packet = b10101010
  Even parity bit: b1
  Total of 5 1’s.
  Where’s the error?
Data packet = b10101010
  Odd parity bit: b1
  Total of 6 1’s

## Slide 8: Parity’s Limitation
Original data packet: b10100001
  Even parity sent as b1.
Receiver gets data packet: b10101011
  Even parity received as b1.
No parity error!
But the data is incorrect.
This limitation is usually called the “Hamming Distance”.

## Slide 9: Hamming Codes
Named for R.W. Hamming
Basically just redundant parity
Looks complicated, but really isn’t.
For any value of n, we generate a value that is 2n - 1 bits. Of these bits:
  n are check bits.
  2n - 1 - n are data bits
  Example: Let n = 3. Then we create a 23 - 1 = 7 bit data packet. 3 bits are check bits. 4 bits are data.
  Example: We want check bits for 32-bits of data. n = 5 only covers 26 data bits, so we need 6 check bits.

## Slide 10: Creating a Hamming Code
Lay out the bits in a line and number them from 2n - 1 down to 1. If the bit is a power of 2 (1, 2, 4, etc.) it is a check bit.
For all of the other bits, if the binary representation of that bit’s number has a 1 that corresponds to a check bit, that data bit factors into the parity calculation for a given check bit.
Example: Let n = 3. Bit 1 is a check bit, and covers bits 1, 3, 5 and 7 (001, 011, 101, 111). Bit 2 is a check bit and covers 2, 3, 6 and 7 (010, 011, 110, 111). Bit 4 is a check bit and covers bits 5, 6, and 7 (101, 110, 111).

## Slide 11: An Alternate Way of Thinking
Position 1: check 1 bit, skip 1 bit, check 1 bit, skip 1 bit, etc. (1, 3, 5, 7, 9, 11, 13, 15, ...)
Position 2: check 2 bits, skip 2 bits, check 2 bits, skip 2 bits, etc. (2, 3, 6, 7, 10, 11, 14, 15,...)
Position 4: check 4 bits, skip 4 bits, check 4 bits, skip 4 bits, etc. (4, 5, 6, 7, 12, 13, 14, 15, 20, 21, 22, 23,...)
Position 8: check 8 bits, skip 8 bits, check 8 bits, skip 8 bits, etc. (8-15, 24-31, 40-47, ...)
Remember to start with the check bit!

## Slide 12: An Example
A Data Word: b10011010
Insert spots for check bits
  12 11 10 9 8 7 6 5 4 3 2 1
  1 0 0 1 _ 1 0 1 _ 0 _ _
Calculate Appropriate Parity bits
  First bits covered:
  12 11 10 9 8 7 6 5 4 3 2 1
  1 0 0 1 _ 1 0 1 _ 0 _ _
  So:
  12 11 10 9 8 7 6 5 4 3 2 1
  1 0 0 1 _ 1 0 1 _ 0 _ 1

## Slide 13: Hamming Example Continued…
Next Check bit:
  12 11 10 9 8 7 6 5 4 3 2 1
  1 0 0 1 _ 1 0 1 _ 0 _ 1
  So:
  12 11 10 9 8 7 6 5 4 3 2 1
  1 0 0 1 _ 1 0 1 _ 0 1 1
Bit 4:
  12 11 10 9 8 7 6 5 4 3 2 1
  1 0 0 1 _ 1 0 1 1 0 1 1
Bit 8:
  12 11 10 9 8 7 6 5 4 3 2 1
  1 0 0 1 0 1 0 1 1 0 1 1

## Slide 14: Hamming Concluded
Final Data To Send:
  12 11 10 9 8 7 6 5 4 3 2 1
  1 0 0 1 0 1 0 1 1 0 1 1
It is often more convenient to separate the check and data bits:
  12 11 10 9 8 7 6 5 4 3 2 1
  1 0 0 1 1 0 1 0 0 1 1 1

## Slide 15: Detecting Errors with Hamming
So our “mixed” data word is b100101011011.
What if we got b101101011011?
  We can easily tell that bit 10 is flipped because we can see both ends of the communication.
How does the average receiver detect errors?
Recalculate parity on each of the check bits.
  Parity errors at bit 8 and bit 2 (check bits = b1010)
  8 + 2 = 10 (and b1010 = 10)
  Correction applied by just flipping that bit.
If two bits are flipped, the parity will be screwed up, but we won’t be pointed to a specific bit.

## Slide 16: So What?
Hamming is the most traditional way of applying ECC to things like RAM and other data transfers.
  At least the ones that don’t use CRC.

## Slide 17: CRC
Cyclic Redundancy Check
A hash function creates a checksum that is transmitted along with the data.
  There are lots of “approved” hashes.
Checksum is generated by the transmitter and receiver, based on the data.
  Mostly an XOR operation.
If the checksum doesn’t match, there was a problem.
CRC-32 is the polynomial hash function for PNG, Ethernet and ZIP.
The error detection and correction distance is highly tied to the polynomial itself.

## Slide 18: Summary
Parity
  Hamming distance of 2.
  Even or odd.
Bit Stuffing
  Attempts to prevent “stuck-at” errors and the reception of special bit sequences.
  Sticks a 0 in after 5 1’s in a row.
Hamming Codes
  Multiple even parity bits allow us to pinpoint the bit that flipped.
  Hamming distance of 3.
CRC
  Hash function that generates a checksum, verified by the receiver.