## Slide 1: EE 3173 Lecture 2
Nios II Architecture

## Slide 2: Lecture 2 Concepts
Nios II Architecture
  Basically, what are the defining features of the Nios II, its instruction set, its operation and design flow.
Credit: Most of these slides are borrowed from Dr. Brian Davis, who borrowed them from Dr. Kieckhafer, who probably borrowed them himself. This is how college teaching goes.

## Slide 3: The Target Platform
Altera Nios Development Kit – Cyclone Edition

## Slide 4: Nios II
Altera Nios II is a soft microprocessor “core”
  Exists as configuration & the describing file(s)
  The hardware description can be downloaded onto an FPGA after compilation to partition, place & route
Comes in three cores sizes/types
  Nios II/e - Economy. Small physical size, low performance
  Nios II/s -- Standard. Study in tradeoffs, used in Tutorial
  Nios II/f – Fast. Blazing performance, big physical size.
  Added flexibility – Cache sizes in each core
  Peripherals – added arbitrarily using SOPC builder
Target Application = embedded microcontroller

## Slide 5: Nios II Development flow
System (SOPC) design
Parallel Hardware & Software design
  Both dependant upon system design
Software dependant upon the hardware definition
  (base addresses, etc)
Allows for iterative design

## Slide 6: Development Flow
Critical Steps:
  Generate – take user description & produce hardware description & required files (header & system spec) for software development
  Parallel ancillary hardware & software development
  Compile – target complete hardware design for specific FPGA
  Compile software for target defined in generate
  Test via simulation or execution on FPGA
Iterative process
  Determine if hardware meets requirements or could be improved
  Allows hardware/software tradeoffs
Allows for optimizing along the critical path
  Slack: Time between the stability of the longest delay signal & latching clock edge
    Produced through simulation
  Simulation identifies critical path & the Verilog comprising this path can be tweaked

## Slide 7: SOPC Builder
Each SOPC Builder system is represented by a file named <system module name>.ptf
  PTF: plain-text file describing the structure of the system and other system-specific details.
  In a purely mechanical sense, the SOPC Builder GUI is a .ptf file editor.
The generate process converts the PTF to a Verilog description of the system

## Slide 8: SOPC Builder GUI
Far easier than developing the Verilog yourself
Has significantly improved over recent versions (or so I am told)
Handles many of the mundane chores without tedium
  Busses
  Address decoding

## Slide 9: Represented System
Note Avalon Switch Fabric
An arbitrary number of each functional unit is supported

## Slide 10: Open Core Issues
A possible licensing issue in the lab
Altera has many licensing levels for the Nios II IP
Open Core is (I believe) allowed use of Altera IP in which they maintain control & do not allow arbitrary user usage
LM_LICENSE file
  With the proper file, we have the ability to use, download & modify the SOPC builder generated files
  It appears with the current license we can only keep the FPGA operating with a process on the CPU.
  We hope to have this resolved

## Slide 11: JTAG
Joint Test Action Group
IEEE 1149.1 standard entitled “Standard Test Access Port and Boundary-Scan Architecture for test access ports”
Originally used for testing printed circuit boards
4 or 5 pin interface
      TDI (Test Data In)
      TDO (Test Data Out)
      TCK (Test Clock)
      TMS (Test Mode Select)
      TRST (Test Reset) optional.
Designed so that one or more chips can have their state space scanned in & out
  Used to initialize machine state on Altera Cyclone board
  Also can be used to scan out state for debug purposes.
  chips on a board
Cyclone board HAS JTAG support
JTAG support CAN optionally be generated into a Nios II design

## Slide 12: Nios II Processor Implementation
“ The functional units of the Nios II architecture form the foundation for the Nios II instruction set. However, this does not indicate that any unit is implemented in hardware. The Nios II architecture describes an instruction set, not a particular hardware implementation. A functional unit can be implemented in hardware, emulated in software, or omitted entirely” – Nios II Processor Reference Handbook

## Slide 13: Nios II Implementation
The Nios II is an Architecture, whereas the Nios II/e or Nios II/f is an organization
Altera provides multiple cores for different design objectives.
What is a functional unit?
  Adder, branch unit, multiply, load/store
  Can you think of multiple ways to do these?
    Is there a cost (gates), speed, simplicity tradeoff?

## Slide 14: Nios II Block Diagram

## Slide 15: Nios Core Characteristics
DMIPS – Dhrystone MIPS
  Embedded systems benchmark
  Meaningless Indicator of Processor Speed
The Cyclone EP1C20 will not run @ the fMAX frequencies
Range of features over the range of organizations

## Slide 16: More Core Characteristics

## Slide 17: Multiple-layer Flexible Design
The Nios ISA is fixed
  Sorta.
Nios II core
  The processor organization/implementation is flexible
    Varied area, pipeline stages, cache, CPI, performance
  Altera has provided three Processor organizations
    /f, /s & /e
  Not advised for user modification – but it is possible
Hardware Design
  Includes the peripherals & on-chip interconnect – buses
    UARTs, SPI, PIO, timer, JTAG & memories
  Altera has provided five hardware designs
    Standard, Full-Featured, Fast, Small, Low-Cost
    And you have built one design – from the Tutorial
  Advised for user level system design – starting points provided by Altera

## Slide 18: Hardware Design Examples Specifications
Specification | Standard | Full-Featured | Fast | Small | Low- Cost
Board Support | Stratix® II, Stratix, Stratix Professional, Cyclone™ & Cyclone II Versions | Stratix II, Stratix, Stratix Professional, Cyclone & Cyclone II Versions | Stratix II, Stratix & Stratix Professional Versions | Stratix II, Stratix, Stratix Professional, Cyclone & Cyclone II | Cyclone & Cyclone II Versions
Nios II Core | Nios II /s 4 Kbytes d-cache | Nios II /f 4 Kbytes i-cache 2 Kbytes d-cache Hardware Multiply | Nios II /f 4 Kbytes i-cache 2 Kbytes d-cache Hardware Multiply | Nios II /e No Cache | Nios II /e No Cache
(JTAG) Debug Module | Yes | Yes; Hardware Breakpoints; Trace Enabled | Yes | No | Yes
On-Chip RAM | 64 Kbytes (1) (Stratix Version Only) | 64 Kbytes (1) (Stratix Version Only) | 64 Kbytes | 2 Kbytes | 4 Kbytes
Off-Chip RAM Interface | 1 Mbyte | 1 Mbyte | - | - | -
(CFI) Flash Interface | 8 Mbytes | 8 Mbytes | - | - | -

## Slide 19: proc Characteristics
Issues to consider when studying a new processor
Also a good outline for comparing two processors
  1. What does the pipeline look like?
  2. What is the register structure?
  3. What data types are supported?
  4. What unusual or “interesting” instructions exist?
  5. What is the subroutine call/return sequence like?
  6. What are its memory management conventions?
  7. How are exceptions and interrupts handled?
  8. How does it support co-processors?

## Slide 20: proc Characteristics
1. What does the pipeline look like?
2. What is the register structure?
3. What data types are supported?
4. What unusual or “interesting” instructions exist?
5. What is the subroutine call/return sequence like?
6. What are its memory management conventions?
7. How are exceptions and interrupts handled?
8. How does it support co-processors?

## Slide 21: Nios II Pipeline
What will be the consequences of # pipeline stages?
  Increased cost
    Pipeline stage overhead -latches
  Reduced period
    Increased Frequency

## Slide 22: Pipelining in 1 slide
Increased # of stages allows reduced CPI – cycles per instruction
The goal is a CPI = 1
  Fixed length instruction (Fetch = 1 cycle)
  A single Memory I/O per instruction (Memory cycle)
  Limit the amount of computation per cycle
Reduced period (i.e. increased Frequency) with
Pipeline Hazards
  Data, Control & structural hazards result in CPI
Superscalar – put these things in parallel for CPI (theoretically) < 1
Fetch
MIPS ADD
LOAD
BEQ
Decode
Memory
Execute
Write Back
Fetch
Decode
Memory
Execute
Write Back
Fetch
Decode
Memory
Execute
Write Back

## Slide 23: Nios II/e
Basic, straightforward RISC architecture
Multiple cycles per instruction
Small & inexpensive
But slllloooowwww…

## Slide 24: proc Characteristics
1. What does the pipeline look like?
2. What is the register structure?
3. What data types are supported?
4. What unusual or “interesting” instructions exist?
5. What is the subroutine call/return sequence like?
6. What are its memory management conventions?
7. How are exceptions and interrupts handled?
8. How does it support co-processors?

## Slide 25: Nios II Register File
32 general-purpose integer registers
  fixed 32-bits apiece – same as instruction length
  Fully utilized 5-bit identifiers
(6) control registers, 32-bit each
  Architecture supports supervisor and user modes that allow system code (i.e. Verilog) to protect the control registers from errant applications.
The Nios II architecture allows for the future addition of floating point registers.

## Slide 26: Register Functions
Procedure calling convention
  Some architectural
    Zero
    SP, FP
    Return Addr
  Some by convention only
    Caller-saved
    Arguments
  Interface between Compiler, Assembler & ISA

## Slide 27: proc Characteristics
1. What does the pipeline look like?
2. What is the register structure?
3. What data types are supported?
4. What unusual or “interesting” instructions exist?
5. What is the subroutine call/return sequence like?
6. What are its memory management conventions?
7. How are exceptions and interrupts handled?
8. How does it support co-processors?

## Slide 28: Architectural Data Types
All 32-bit data types
16-bit sign extended immediate
Limited 64-bit support – multiply
Registers are set up for 64 bit support
  (2) registers for return values
  Pairs for parameters & caller saved
Floating point – in the future

## Slide 29: Language Data types
Nios II language support
C/C++ Application Binary Interface

## Slide 30: proc Characteristics
1. What does the pipeline look like?
2. What is the register structure?
3. What data types are supported?
4. What unusual or “interesting” instructions exist?
5. What is the subroutine call/return sequence like?
6. What are its memory management conventions?
7. How are exceptions and interrupts handled?
8. How does it support co-processors?

## Slide 31: Instruction Formats
32-bit fixed-length instructions
  RISC – fixed, few, reduced, consistent
  6-bit opcode for all types
I-type
  16 bit Immediate
  (2) 5-bit register identifiers A & B
  Arith/Logic, branch, load/store, cache management
R-type
  (3) 5-bit register identifiers A, B & C
  11 bit opcode extension OPX
  Arith/Logic, comparison, custom inst
J-type
  26 bit immediate
  Currently only CALL (i.e. long jump)

## Slide 32: Instruction Formats
Consistent format
Few formats – MIP(5), 80x86(huge #)
  Allows for fast operation
  Still allows a wide set of instruction categories

## Slide 33: Instruction Categories
Data Transfer instructions
Arithmetic & Logical
Move
Comparison
Shift & Rotate
Program Control
Other Control
Custom

## Slide 34: proc Characteristics
1. What does the pipeline look like?
2. What is the register structure?
3. What data types are supported?
4. What unusual or “interesting” instructions exist?
5. What is the subroutine call/return sequence like?
6. What are its memory management conventions?
7. How are exceptions and interrupts handled?
8. How does it support co-processors?

## Slide 35: Call / Return Sequence
Primary Problems in a recursive language:
  Return Address
  Passing parameters and return variables
  Storing the called routine’s local variables
Solution: Use “run-time stack” for procedure linkage
Stack Frame 
  The collection of data required by a given routine
    return address, local variables, params & return vars

## Slide 36: Example Stack Convention
Each unit is a stack frame
Frame specifics differ between architectures & even compilers

## Slide 37: Call / Return Sequence
Stack Pointer (SP) register =
  The register holding the address of top of stack
Memory Allocation:
  Code and Data memory space starts at lowest address (00..00) and grows into higher addresses
  Run-Time stack starts at highest address (FF..FF) and grows into lower addresses

## Slide 38: Nios II Stack

## Slide 39: Subroutine Call Instructions

## Slide 40: Subroutine Call/Return Sequence
CALL = standard call instruction
  Branches to subroutine
  stores return address in ra (r31)
    Syntax: CALL label:
      ra ← PC + 4
      PC ← (PC31..28 : IMM26 × 4)
    CALL %rA
RET = return from subroutine
  Returns from subroutine – using return address stored by CALL instruction
  syntax: RET
      PC ← ra
  The only storage of state in the instruction set architecture is the return address
  The remainder of the run-time stack is managed by software

## Slide 41: Register Usage
Args & Return are set up for 64-bit data
Each procedure has at least 14 registers for local use
Not truly a general purpose register file

## Slide 42: Stack Management -- In C
Stack is managed by software convention

## Slide 43: Call/Return in Other ISAs
Instructions to support context switching
  Context switching when O.S. changes processes
  must save entire processor state, including:
    PC
    CC's
    PID
    All data registers (this is one argument for fewer regs)
  Better left to Operating System, rather than to special instr.
Instructions to assist procedure call and return
  Very common action in real software
  Mostly run-time stack management
  Worthy of its own major topic

## Slide 44: proc Characteristics
1. What does the pipeline look like?
2. What is the register structure?
3. What data types are supported?
4. What unusual or “interesting” instructions exist?
5. What is the subroutine call/return sequence like?
6. What are its memory management conventions?
7. How are exceptions and interrupts handled?
8. How does it support co-processors?

## Slide 45: Nios II Memory management
Caches
  Instruction & Data – utilize M4K
Tightly Coupled Memory
  Basically Software managed cache - utilize M4K
    guaranteed low-latency memory
    access for performance-critical application
    Software can guarantee that performance-critical code or data is located in tightly coupled memory
    No real-time caching overhead, such as loading, invalidating, or flushing
  Memory mapped using SOPC builder
Off Chip Memory
  SRAM
  DRAM
  Flash
  Compact Flash

## Slide 46: Avalon Switch Fabric
Not a Bus
Encompasses a hierarchy in the “fabric”
Encompasses
  Address decoding
  Components
    Address
    Data
    Control/ Command
  Latching
  Up to 128 bit width

## Slide 47: Peripherals
Separate I/O address space
  Requires separate instructions
  As used in x86 architecture
  The entire I/O address space is peripherals or unutilized
Memory Mapped I/O
  Uses the same instructions as LD/ST
  Typical of RISC architectures, used in Nios II

## Slide 48: Nios Peripheral devices
Have a library of peripherals to choose from, including:
  Two types of serial interface
  Parallel port
  Timer
And of course, you can always design your own

## Slide 49: proc Characteristics
1. What does the pipeline look like?
2. What is the register structure?
3. What data types are supported?
4. What unusual or “interesting” instructions exist?
5. What is the subroutine call/return sequence like?
6. What are its memory management conventions?
7. How are exceptions and interrupts handled?
8. How does it support co-processors?

## Slide 50: Interrupts
Hardware level support for acquiring CPU attention
  Useful for minimizing latency & high level of temporal accuracy (PWM, input capture, etc)
Similar to procedure calls – performed unexpectedly by hardware or software
  Interrupt (synchronous, device generated)
    Maskable: device-generated, associated with IRQs (interrupt request lines); may be temporarily disabled (still pending)
    Nonmaskable: some critical hardware failures
  Exceptions (asynchronous)
    Processor-detected
      Faults – correctable (restartable); e.g. page fault
      Traps – no re execution needed; e.g. breakpoint
      Aborts – severe error; process usually terminated (by signal)
    Programmed exceptions (software interrupts)
      int (system call), int3 (breakpoint)
      into (overflow), bounds (address check)

## Slide 51: General Interrupts
Non-vectored exception controller to handle all exception types
  All exceptions, including hardware interrupts, cause the processor to transfer execution to a single exception address
  Nios II supports nested interrupts
  Nios II has 32 level-sensitive interrupt requests (IRQ0 – IRQ31)

## Slide 52: Hardware Exceptions
A hardware interrupt is generated if and only if all three of these conditions are true:
  The PIE bit of the status register is 1
  An interrupt-request input, irqn, is asserted
  The corresponding bit n of the ienable register is 1
Exceptions are installed by
  Assigning IRQ in SOPC Builder
  Installing an Interrupt Service Routine (ISR) int alt_irq_register (alt_u32 id, void* context, void (*isr)(void*, alt_u32));
  Enabling (PIE & IENable) in software

## Slide 53: Vector Table
More traditional to have interrupt vectors for each IRQ
  Tradeoffs : faster, more address space, less complex ISR, more complex general exception handler
Vector Tables
    reset address
    exception address
    break handler address
    ISR handler addresses

## Slide 54: proc Characteristics
1. What does the pipeline look like?
2. What is the register structure?
3. What data types are supported?
4. What unusual or “interesting” instructions exist?
5. What is the subroutine call/return sequence like?
6. What are its memory management conventions?
7. How are exceptions and interrupts handled?
8. How does it support co-processors?

## Slide 55: Co-processors
A coprocessor is a computer processor used to supplement the functions of the primary processor (the CPU).
Operations performed by the coprocessor may be floating point arithmetic, graphics, signal processing, string processing, or encryption.
Co-processors are more common in the past when an entire CPU could not be contained on a single ASIC
  80386 – Integer processor ; 80387 floating point processor
More common in modern systems are Multiprocessors
  Co-processors are subordinate by hardware architecture
  Multiprocessors may be peers, subordinate by hardware or subordinate by software

## Slide 56: Multi-processors
Multi-processor does not necessarily mean symmetric multiprocessor (SMP) where all are equal
    Some (Dual Core Pentium 4) may be both SMP & CMP
  Symmetric Multiprocessors (SMP)
  Chip Multiprocessors (CMP)
    CELL Multiprocessor (PPE & SPEs) (Playstation 3 & other Apps)
  Simultaneous Multi-Threading (SMT)
SOPC Builder supports multiple Nios II CPU in each hardware design
  May be designed symmetric or disparate architecture
Requires a FPGA of significant size – you can figure this out from resource usage
Share a common Memory Map
  Some peripherals may be unique
  Some peripherals (primarily memory) may be shared

## Slide 57: Co-processors
How do parallel processors communicate?
  Shared Memory
  Message Passing
Nios II uses a shared memory architecture
Even shared memory multiprocessors frequently pass messages

## Slide 58: Why Multiple Processors?
Partitioning of workload
  Distribute workload (User Interface, DSP, xmit/recv load/store)
  Each processor can be designed for that specific function
  Each processor may be able to be more Real-Time when workload is limited
Increased performance
  Requires partitioning the workload
  This is how supercomputers work
    http://www.top500.org
  But with a Nios II – just go with a more powerful processor
Redundancy
    Some Multi-Core processors are redundant & self-checking
Multiprocessor Courses
  EE 5772 - Parallel Computer Organizations
  CS 5331 - Parallel Algorithms
  CS 5431 - Advanced Computer Architecture

## Slide 59: Nios II Concluded
Will remain the centerpoint of the lab
Assembly language programming later in the semester
Significant Nios II content on Exams

## Slide 60: Chapter 2
Very little Content
Brief History
    ENIAC – first Hardware
    vonNeumann – important concepts of stored programs of instructions with implications to today
Designing for performance
    Unusual place for DRAM
    Covered generations of computers already
proc Evolution
    x86 : 4004…8008…8080…8086…80186 (still popular controller) …80286…80386…80486…Pentium…Pentium Pro…Pentium2…Pentium3…Pentium4
    RISC vs. CISC
    VLIW, EPIC, SMT

## Slide 61: Lecture 2 Summary
Nios Architecture is very RISC-y and very straightforward.
We’ll spend a lot of time in lab playing with the Nios, and won’t talk much more about it in class.
Remember our 8-point “Get To Know You” guidelines for examining a new processor architecture.