## Slide 1: EE 3173 Lecture 8
PCI, PCI 2.2, PCI-X

## Slide 2: Recap
Busses
  Timing
    Synchronous, Asynchronous, Isochronous
    Motivations & Timing Diagrams
    Signals – Valid times & latching times
  Bus Arbitration
    Bus Arbiter, Bus Master, Bus Slave
    General Arbitration Sequence
    REQ, GNT, BSY signaling
    Centralized vs. Distributed
    Arbitration organizations
      These are not the only types
      Independent Request Arbitration
      Poll Counter Arbitration
      Daisy Chain Arbitration
  Error Detection and Correction
    Parity, ECC, Bit Stuffing, CRC

## Slide 3: Bus Technologies
Many proprietary busses
  Avalon (Nios)
  Control/Address/Data bus (PC)
  Unibus (DEC-PDP)
  MicroChannel Architecture (MCA)
    IBM PS/2 Disaster
Drive for Standardization
  PCI – Peripheral Component Interconnect
  SPI – Serial Peripheral Interconnect
Reduced development costs
  No need to write standards
  Re-use of IP
  Fabless companies
  Fab provided design environment
  Fab = Circuit Fabrication

## Slide 4: Bus Interconnection
All interconnections are possible
  Differ in the cost and bandwidth
  Busses appropriate for:
      FSB: high-speed, many signals
      PCI: In-case peripheral interconnect
      USB: Few signals, longer cables, more devices
Some high-bandwidth chip-to-chip Protocols
  Arapahoe/3GIO (Became PCI Express)
  HyperTransport
  Infiniband
  RapidIO

## Slide 5: PCI Introduction
PCI = Peripheral Component Interconnect
  Designed as a high-speed I/O bus
Developed by Intel
  Needed high bandwidth bus for Pentium systems
  Designed to be “processor independent”
    But has several classic Intel features
  Designed to need minimum of “support” chips
    mostly “bridges” to other busses
Public Domain Bus Architecture
  PCI SIG = PCI Special Interest Group
  The governing body for PCI specifications

## Slide 6: PCI Bus
Appropriate for in-case peripherals
  NIC
  Mass storage controller
  Data acquisition device
Synchronous: single phase clock
Bus width: 32-bits or 64-bits
Multiplexed Address/Data Lines (AD)
  Address and data use the same physical lines
  Must send address and data sequentially
    In the “old days” chip pins were at a premium
    needed to minimize number of pins / chip package

## Slide 7: I’m Sure This Means Something

## Slide 8: Simple System Application
PCI is a mid-level bus
  In chassis – high speed signals
  Wide bus 32/64 bits
  Constrained # of devices
  Limited length

## Slide 9: PCI Specification History
www.pcisig.com
  Costs $2500 to join for specification, many documents available for free
Original (1992) 33 MHz
Ver 2.1 (1995) 66 MHz
  Ver 2.2 primarily a clarification of 2.1
  also implements “hot plug” spec for on-line swapping
PCI-X (1999) 133 MHz
  Ver 3.0 clarify PCI-X & changes made since 2.2
PCI Express (first devices 2004) 2.5 GHz
  Serial – no longer slot-backwards compatible
  Scalable bandwidth – using variable width configurations (# lanes)
Others
  Low-Profile PCI = smaller card profile
  Mini-PCI = laptop & other mobile applications
  Compact-PCI = Ruggedized for embedded systems
    expensive & slow (33MHz)

## Slide 10: PCI 2.2 Specifications
Four possible PCI configurations
Currently 98+% of systems & cards are slowest possible configuration
More bandwidth is only needed for:
  High speed networking (1 Gbit+ Ethernet)
  RAID (Redundant Arrays of Independent/Inexpensive Disks) controllers

## Slide 11: PCI - X
Previous generation Peripheral Component Interconnect
Bandwidth approaching 1GByte/sec
  Operates at 64 bits, 3.3v signaling, 133 MHz
  Legacy Cards will fit into PCI-X slots
Optimizations include:
  Split transactions and transaction-byte counts that improve the efficiency
  Increased utilization of bandwidth
  Reduced power consumption

## Slide 12: Performance History

## Slide 13: PCI & Application Bandwidth

## Slide 14: PCI Bandwidth Utilization
www.serverworks.com/technology/ pdf/PCI-X_2-0_WhitePaper.pdf

## Slide 15: Nomenclature
Initiator = Bus Master
Target = The Active Bus Slave
Transaction = 1 transfer of data
  May contain multiple data items
  supports burst operations
# = Active-low signal (e.g. IRDY# or TRDY#)
CK = PCI Bus Clock (single phase)
  Synchronization Protocol:
    ASSERT & CLEAR all signals on falling edge
    SENSE (or sample) all signals on rising edge

## Slide 16: Performance Features
Very Flexible Protocol
  Can do very complex operations
  Can serve complex, sophisticated devices
  Needs several extra signals 
    Simple ops may seem unnecessarily complex
Turnaround Cycle
  Constraint for lines with >1 source (e.g. AD)
  Must wait 1 clock cycle before changing source
  The 1 idle cycle guarantees no contention
  Example: AD lines on a “read” operation

## Slide 17: Pin Layout for PCI Devices

## Slide 18: “Interesting” Signal Lines - 1
AD = Address/Data (32 bits or 64 bits)
  Meaning depends on “phase” of transaction
Address Phase  AD carries address of “target”
  Exactly 1 address phase per transaction
  lasts exactly 1 clock cycle
Data Phase  AD carries data
  May be several data phases in 1 transaction
  Each data phase transfers one item (word)
  multiple phases/transaction allow “burst” transfers
  coincidentally supports Intel “block move” instructions

## Slide 19: “Interesting” Signal Lines - 2
C/BE# = Command/Byte Enable (4-bits or 8-bits)
During Address Phase:
  Sends command to target device
  Defines direction of transfer, type, duration, etc
  More details later
During Data Phase:
  Indicates which bytes of AD lines hold valid data
  Simplifies communication with < 32-bit devices
  Have 1 C/BE# bit for each byte of AD
    32-bit AD  4-bit C/BE#
    64-bit AD  8-bit C/BE#

## Slide 20: “Interesting” Signal Lines - 3
Transaction Synchronization Signals
  FRAME# (1 bit)
    Asserted by Initiator at start of transaction
    Cleared at start of final data phase of transaction
  DEVSEL# (1 bit)
    Asserted by target when it recognizes its address
    indicates target device has been “selected”

## Slide 21: “Interesting” Signal Lines - 4
Phase Synchronization Signals
    allows either partner to extend a phase
    supports different speed devices (wait states)
  IRDY# = Initiator Ready (1-bit)
    Read  Initiator is ready to receive data
    Write  The AD lines contain valid data
  TRDY# = Target Ready (1-bit)
    Read  The AD lines contain valid data
    Write  Target is ready to receive data

## Slide 22: PCI 1-Word Read

## Slide 23: PCI Multi-word Read
3 Data Phases
Either Initiator or Target can stretch data phases
  IRDY# & TRDY# signals
Assume:
  Target needs to stretch 2nd data phase
  Initiator needs to stretch 3rd data phase
That brings us to Stallings, Fig 3.22

## Slide 24: PCI Read - Waveform

## Slide 25: PCI Read - Events Sequence
(a) Init: assert address, C/BE (command), FRAME
(b) Tar: recognize its address (no changes)
(c) Init: clear AD (turnaround), assert C/BE, IRDY
(d) Tar: assert data, DEVSEL and TRDY
(e) Init: latch data and set C/BE for next item
(f) Tar: clear TRDY, wait til ready, assert TRDY
(g) Init: clear IRDY (due to internal stall)
(h) Init: set IRDY, clear FRAME for final item
(i) Init: clear IRDY, CB/E Tar: clear AD, TRDY, DEVSEL

## Slide 26: PCI Write

## Slide 27: PCI Write Stages
FRAME# is asserted along with a bus command and address data.
The data immediately follows the address (no turn-around cycle!) and IRDY# and TRDY# are asserted.
Data is transferred as long as IRDY# and FRAME# are asserted.
When both IRDY# and FRAME# are deasserted, then the transaction is complete.

## Slide 28: PCI Bus Commands Overview
Bus Commands
  Control Commands (special operations)
  I/O Commands (Intel separated address space)
  Memory Read Commands (incl. burst)
  Memory Write Commands (incl. burst & cache coherency)
  Configuration Commands (for startup config)
PCI Bus Arbitration
  Independent Request scheme (REQ# & GNT#)
  No BSY line. Uses {FRAME# OR IRDY#}
  Uses “Hidden Arbitration”
    Arbitrates next master during current transaction
  Arbitration priority not a part of the bus spec!

## Slide 29: Bus Commands
Control Commands
  Interrupt Acknowledge
  Special Cycle = identifies a broadcast message
  Dual Address Cycle = 2nd part of a 64-bit address
I/O Commands
    Intel legacy architecture uses separated address space…
    Thus we need separate I/O instructions…
    Which issues separate I/O commands to the bus
  I/O Read
  I/O Write

## Slide 30: Bus Commands
Boot Commands
  PCI devices are not hardwired to addresses and IRQs
  Devices contain addressable “configuration” regs
  Boot routine can:
    read configuration regs to ID device type and needs
    write to configuration regs to initialize the device
  Greatly facilitates “plug and play”
Configuration Read
Configuration Write

## Slide 31: Bus Commands
Memory Read Commands
  Once upon a time PCI was fast enough for a system bus
  Has memory access instructions
  Includes support for cache block operations
Memory Read
  Up to 2 data phases in the transaction
  Meant for 1 word LOAD (incl. double precision)
Memory Read Line
  For 3-12 data phases in the transaction
  Meant for up to 3 cache lines
Memory Read Multiple
  For >12 data phases in the transaction
  Meant for >3 cache lines

## Slide 32: Bus Commands
Memory Write Commands
  Memory Write
    Plain old vanilla write
    Supports plain old vanilla STORE instruction
    can also have multiple data phases
  Memory Write Invalidate
    Meant to support cache write-back
    Useful for multiprocessor systems
      when a write is executed by one processor
      allows cache lines to be invalidated in other procs
      maintains cache coherence between processors

## Slide 33: PCI Bus Arbitration
Uses Independent Request Arbitration
  Signals are REQ# and GNT#
  REQ# and GNT# are point-to-point (private) lines
  Number of signals is installation dependent
Ownership only lasts for one Transaction
  Current owner must re-arbitrate to get next transaction
  But we can extend the transaction
Uses “Hidden Arbitration” 
  Arbitration for cycle N occurs during cycle N-1
  No time is wasted arbitrating between transactions
  The only delay is the 1 cycle turnaround on AD

## Slide 34: Arbitration Signals
PCI has no BSY signal
Combines FRAME# and IRDY# to act as a BSY#
  FRAME# brackets the transaction
    it is asserted immediately
    it is cleared 1 cycle before end of transaction
  IRDY#  “data is valid” or “ready to receive”
    it is asserted at some point after address phase
    it is cleared at end of last data cycle
Logically: BSY# = FRAME# OR IRDY#
  Thus, if either is low, then the bus is busy

## Slide 35: PCI Arbitration Example

## Slide 36: PCI Arbitration Example
Two units, A & B each want to execute a 1-word write
  (a) REQ#_A is previously low (active)
  (b) Unit B asserts REQ#_B, but
  (c) Arbiter has already decided to grant GNT#_A
  (d) A sees GNT#_A & asserts FRAME#, Addr, C/BE#
  (e) Arbiter sees FRAME# = BSY# & arbitrates the next transaction, asserting GNT#_B
  (f) Meanwhile, back at the current transaction:
    A asserts IRDY and the data for the data phase
    A clears FRAME (beginning of last data phase)
    Target asserts TRDY# for the data phase
  (g) B sees GNT#_B & asserts FRAME#, Addr, C/BE#

## Slide 37: PCI Summary
Main Features of PCI Bus
  High-Speed I/O Bus
  Was once fast enough for a system bus
  32/64 bit synchronous multiplexed bus
  clock speed evolution: 33  66  133 MHz
Designed for burst data transfers
  4-bit command specifies operation (C/BE#)
  Transaction sync signals (FRAME#, DEVSEL#)
  Data Phase sync signals (IRDY#, TRDY#)

## Slide 38: References
[1] Syred Data Systems, What is PCI?, unpublished white paper, July 18, 1999, http://www.syred.com/articles/PCI.pdf (current Mar 2002).
[2] Quatech Inc, Data Communication Introduction, http://www.quatech.com/figures/com_ov2001.pdf (current Mar, 2002).