## Slide 1: EE 3173 Lecture 4
Nios II Assembly Language Overview

## Slide 2: Lecture 4 Concepts
A Brief Intro to the “How’s, When’s and Why’s” of assembly language programming.
An Intro to the Nios II Assembly language
A Little Programming Type Stuff

## Slide 3: Efficient Programming
Programming is hard.
  Duh.
Good programming is even harder.
Writing efficient code in a high-level language can be nigh on impossible.
Besides, hardware designers didn’t design the chip for C or Java or Python or whatever. It was designed for its ISA, which is most directly accessed by assembly language programming.

## Slide 4: When Do You Want to Write Assembly?
Realistically, never. It’s even harder to write good assembly than good C.
But there are some exceptions:
  When there’s no compiler for your target architecture.
  When you don’t trust the available compiler or think you know better than the compiler.
  When performance is paramount.
  When code size must be minimized.

## Slide 5: Linux Kernel, Version 2.2.5
In file arch/i386/lib/delay.c:
  #include <linux/sched.h> #include <linux/delay.h> void __delay(unsigned long loops) { int d0; __asm__ __volatile__( “\tjmp 1f \n” “.align 16 \n” “1:\tjmp 2f \n” “.align 16 \n” “2:\tdecl %0\n\tjns 2b” :”=&a” (d0) :”0” (loops)); }
Creates a precise delay -- Not possible with a HLL

## Slide 6: Linux Kernel, 2.2.5
In file include/asm-i386/spinlock.h:
  /* On x86 we implement read-write locks as a 32-bit * counter with the high bit (sign) being the “write” * bit. * The inline assembly is non-obvious. Think about it. */ #define read_lock(rw) asm volatile(“\n1:\t” \ “lock ; incl %0\n\t” \ “js f2\n” \ … and so on.
The code is bit-twiddling with precise timing.

## Slide 7: Compiler vs. Assembler
A compiler takes a high-level language, parses the syntax, builds a symbol table, and creates a file in some sort of “intermediate language”.
  What is the Intermediate Language? It varies by compiler.
    Visual Studio creates files in MSIL.
    GCC used GIMPLE and RTL.
    Older compilers might directly generate assembly language.
An assembler takes a specific set of instructions for a specific processor and generates machine code (and maybe some other stuff).

## Slide 8: Assembly Lesson #0
TMTOWTDI
  (“Tim-toady”)

## Slide 9: Introductory Stuff
3 Instruction Formats
  I, R, J
  See the Processor Reference for details
6-bit opcode means 26 (64) potential opcodes, but not all are used.
Pseudo-instructions
  Sometimes you write a line of code and the assembler transforms it into something else.
  Example: You write bgt rA, rB, label and the assembler turns it into blt rB, rA, label. Why?
    Only need to implement half as many instructions!

## Slide 10: Math Instructions
add, addi
div, divu
mul, muli, mulxss, mulxsu, mulxuu
sub, subi

## Slide 11: Digging Into add

## Slide 12: Digging Into addi
Deal with overflow detection the same way as add.

## Slide 13: So What’s the Difference?
One takes the value of two registers, adds them, and sticks the result in a third register.
The other takes a 16-bit immediate and does the same.
What if you need 17+ bits for your constant?
  movhi rB, %hi(value) ori rB, rB, %lo(value)

## Slide 14: Boolean Logic Functions
and, andhi, andi
nor
or, orhi, ori
or, xorhi, xori
All of these pretty much work the same way as the arithmetic functions and do what you would expect.
NOT and NAND seem to be MIA.

## Slide 15: Getting Data In and Out of Registers
ldb/ldbio, ldbu/ldbuio, ldh/ldhio, ldhu/ldhuio
ldw/ldwio
mov, movhi, movi
movia, movui
stb/stbio, sth/sthio, stw/stwio
Each of the “b” instructions loads/stores a single sign-extended byte of data. The “w” instructions grab a full 32 bits using a funny sum to calculate the final address to access.
The “h” instructions get at high-order bytes (sometimes).
  Low order bytes are set to 0 if loading high-order byte!
  “h” instructions might also get a 16-bit sign-extended value.
The “io” instruction bypass the data cache, if present.
The “u” instructions treat data as unsigned.

## Slide 16: Addressing
All loads and stores use offset addressing.
  Sometimes also called “indexed” addressing.
A register holds a value which is an address.
  Like a pointer!
Then the hardware looks at the address in memory supplied by that register.
Changing the value in the offset register doesn’t change the value in memory!

## Slide 17: Program Flow
Generally, an assembly program will just execute one instruction after another in a nice linear order until it reaches The End.
Two kinds of instructions can change the flow:
  Branches
  Subroutine Calls
  We’ve talked about the latter already. So on to the former!

## Slide 18: Branches
beq - Branch on equal to
bge - Branch on greater than or equal
bgeu - Branch on unsigned greater than or equal
bgt - Branch on greater than
bgtu - Branch on unsigned greater than
ble - Branch on less than or equal
bleu - Branch on unsigned less than or equal
blt - A Tasty Sandwich
bltu - Branch on unsigned less than
bne - Branch on not equal
br - Unconditional Branch

## Slide 19: Some Simple Constructs
I think you can figure out the “if” statements.
for loop:
  movi r16, 10 loop: <stuff> subi r16, r16, 1 bne r16, r0, loop done: <other stuff>

## Slide 20: Another Simple Construct
Switch statement: case1: ldw r16, input_offset(r15) movi r17, 1 bne r16, r17, case2 <case 1 stuff> case2: movi r17, 2 bne r16, r17, case3 <case 2 stuff>
And so on.

## Slide 21: Various and Sundry
# Comments start with the hash/pound sign
Just put these two lines at the top of your program and make the main entry point into your program have the label “main:”
  .global main .text
Setting constants
  .equ UARTtxDataReg, 4
Setting strings
  myDumbString: .asciz “A String”
Doesn’t hurt to put “.data” before big collections of static data.

## Slide 22: Various and Sundry
Want to send a constant character out an I/O device? movi r15, ‘K’ stwio r15, 5(r5) # Assumptions: r5 contains the base address of the peripheral and the appropriate xmit reg is 5 past that.
Why stwio?

## Slide 23: The Stuff at the End
Assembly is hard and lots of no fun.
But sometimes it’s necessary.
Use the Nios II Processor Reference for all the nitty-gritty details.