## Slide 1: EE 3173 Lecture 15
Time-Triggered Buses with TTCAN

## Slide 2: Lecture 13 Concepts
Time-Triggered vs. Event-Triggered
What traffic on a TT bus looks like
How TTCAN is mapped onto CAN
Other TT protocols

## Slide 3: A Brief Survey of Access Models
CSMA -- Carrier Sense Multiple Access
  Everybody checks. If nobody else is sending, feel free to transmit.
  CAN, IEEE 802.11
CDMA -- Code Division Multiple Access
  Multiplexes signals with a crazy scheme
  Traditional cell phones
TDMA -- Time Division Multiple Access
  Everybody has a time slot, and we all take turns. Aren’t we nice?
  GSM cell phones, TTCAN, other TT protocols

## Slide 4: Maybe This Helps?
As a trivial comparison imagine a UN party where couples from different countries are invited.
  TDMA: Each couple takes turns talking. They talk for a short time and then stop to let another couple talk.
  CDMA: Each couple talks at the same time; however they all use different languages.
  With TDMA, nobody talks over anybody else.
  With CDMA, nobody understands anybody else, and ignores the “noise”.

## Slide 5: CAN is Event-Triggered
When something occurs at a given node, it causes that node to want to transmit a message.
  What was the timeframe of the last sent message? Who cares? I have something to send now.
Large periods of time could pass with an idle bus.

## Slide 6: TTCAN is Time-Triggered
Things occur on a schedule.
It’s been precisely 33 µs since my last transmission, so it’s time to send something out again.
Nothing changed? Oh well.

## Slide 7: The Schedule
All time-triggered events occur on a rigid, predetermined schedule.
That means the network topology must be known a priori, and cannot change without creating a new schedule.

## Slide 8: But, but why?
What is the point of time-triggered communications? It seems like there’s a lot of wasted bandwidth.
For real-time systems, the key is being able to guarantee a worst-case latency.
  I.e., A node will respond to an input within 150 ms.
Time-triggered protocols guarantee access to the bus with a bounded latency.
  Very important for x-by-wire systems in vehicles. Imagine a steer-by-wire system where the steering wheel sensor couldn’t get on the bus to transmit its message to the wheel actuators.

## Slide 9: Sample Automotive Network

## Slide 10: Current Time-Triggered Networks
TTP -- Time Triggered Protocol
  Developed by TTTech. Very heavy-duty protocol.
  Generally eschewed by automotive suppliers because it’s too robust.
TTCAN
  A time-triggered software layer on top of plain-vanilla CAN.
FlexRay
  Currently the de facto TT protocol for automotive applications (or should be soon).
  Core members of the FlexRay Consortium: BMW, DaimlerChrysler, Bosch, Freescale, General Motors, Philips, Volkswagen

## Slide 11: TTCAN
The goal of time triggered operation on CAN is to avoid latency jitters and to guarantee a deterministic communication pattern on the bus.
Moreover, this allows use of the physical bandwidth of a CAN network much more efficiently (under the constraint of determinism).
Two levels:
  Extension level 1 guarantees the time triggered operation of CAN based on the reference message of a time master.
  In extension level 2, a globally synchronized time base is established and a continuous drift correction among the CAN controllers is implemented.

## Slide 12: Jitter
Here we’re simply referring to a delay in when a message would like to be sent and when it can actually be sent.
  That is, when no other devices want the bus for a higher-priority message.
Jitter in real-time systems is a problem, especially in x-by-wire systems.

## Slide 13: Fleshing Out the Schedule
The Reference Message
  Somebody has to take the role of time master and send out a Reference Message that begins a basic cycle.
  The basic cycle is one of potentially many different schedules that play out between Reference Messages.
  In essence, the RM acts like an SOF in USB.
  Level 1 RMs are just empty data frames.
  Level 2 RMs potentially contain more control information.

## Slide 14: More Schedule
Between RMs are various chunks of time:
  Exclusive Windows
  Arbitrating Windows
  Free Windows
There can be any multiple of these, including multiple exclusive windows for any given device.

## Slide 15: Exclusive Windows
For periodic messages
Will be as long as needed to send the specific message
  Which means the system designer needs to know ahead of time how large each message will be
Could, theoretically, get stomped on by normal arbitrated CAN traffic
  It is, after all, still a CAN bus
Automatic retransmission is not allowed

## Slide 16: Arbitration Windows
If some error condition arises that simply can’t wait, we can revert back to normal CAN bus traffic and transmit our message.
The timeframe for this is still limited, so it probably needs to be short and sweet.
The system designer still has ultimate freedom here, so there can be room for multiple nodes to transmit spontaneous messages.
Automatic retransmissions are not allowed in arbitration windows either.

## Slide 17: Free Windows
Used for future system expansion.
They can be changed to arbitrating or exclusive time windows if new nodes need further space for communication or the bandwidth has to be extended for existing nodes.

## Slide 18: Network Ignorance
Not quite as strong as regular CAN.
A TTCAN node knows when it’s allowed to transmit and when the nodes it’s interested in will be transmitting.
However, it is blissfully ignorant of everybody else.

## Slide 19: The System Matrix
Sometimes a single basic cycle isn’t flexible enough for our system.
  Actually, this is usually the case!
So we can have an arbitrary number of sequential basic cycles.
Obviously, programming the nodes becomes less trivial.

## Slide 20: Multiple Arbitrating Windows
Multiple sequential arbitration windows can be treated as one long window.
An upshot is that, for a change, retransmissions are allowed provided they will fit in the window.

## Slide 21: The Time Master

## Slide 22: The Time Master
Level 1 Time Master
  Not very comprehensive. The standard CAN bit clock is used, and time is all relative to that.
  Everybody synchronizes to the SOF bit of the reference messages.
Level 2 Time Master
  Time is based on a “real” second. Each node synchronizes to the SOF bit, but also verifies their clock is the same as the Global Time sent in the RM.
  Well, not exactly the same. Each node is aware of the delay time between transmission and reception.
  Additionally, nodes attempt to compensate for different rates of clock drift between the local time and the global time.

## Slide 23: Fault Tolerance in the Time Master
N-module Redundancy
  Multiple nodes are ready and willing to be time master, and will automatically step up if some unusual latency is detected on the reception of the RM.
  If a higher-priority Time Master starts transmitting, the lower-priority TM notices and backs off.

## Slide 24: A Flexible Protocol
If supported by all nodes, the Time Master can declare that we’re (temporarily) done with this whole “time-triggered” stuff and go asynchronous for a time.
This is generally not the case for other TT protocols.
  But is largely the result of mapping a software TT protocol onto vanilla CAN.

## Slide 25: The Future of All This
CAN, in cars at least, is dead.
TTCAN was only an interim solution.
The main options at this point are TTP and FlexRay.
  Let’s look at a comparison.
My impression is that FlexRay is winning this battle in the automotive space, with suppliers simply feeling that TTP is overkill.
  The first FlexRay vehicle was a BMW 5-series, so FlexRay is out there. Not in Houghton, obviously.