## Slide 1: EE 3173 Lecture 7
Verilog Refresher
Or
All the Stuff You Should Have Learned in EE 2171 if We Actually Had Enough Time to Teach it to You.

## Slide 2: Concepts
A Brief History of Verilog
Basic Verilog Syntax
Verilog Design Styles
More Advanced Syntax

## Slide 3: Verilog
One of a class of hardware description languages.
Developed in 1984 with a C-like syntax.
Now IEEE 1364
  Verilog95 and Verilog01
Alternative is the DoD-approved VHDL
  Another newer challenger: System C
Future development under the auspices of Acellera
Key Concept: Execution is not strictly linear!

## Slide 4: Really Simple Verilog
module example1(x1, x2, x3, f); input x1, x2, x3; output f; and(g, x1, x2); not(k, x2); and(h, k, x3); or(f, g, h); endmodule

## Slide 5: Module Example1 Unpacked
Implements function
  f = (x1 • x2) + (~x2 • x3)
Is a structural specification
  Structural design is easier, but more time consuming
  Is not really appropriate for large designs
Note that we need intermediate values to “force” sequential execution.

## Slide 6: Behavioral Specification
This is more common, especially for larger designs.
This specific style is called dataflow modeling.
module example3(x1, x2, x3, f); input x1, x2, x3; output f; assign f = (x1 & x2) | (~x2 & x3); endmodule

## Slide 7: Adding a Level of Abstraction
module example5(x1, x2, x3, f); input x1, x2, x3; output f; reg f; always @(x1 or x2 or x3) begin if (x2 == 1) f = x1; else f = x3; end endmodule

## Slide 8: A Few Details
Comments
  Single line: //
  Multi-line: /* … */
begin and end
  Replace { and }, respectively
Code in an always block is executed sequentially.
Verilog compilers are not nice.
Check out my little experimental text.

## Slide 9: Another Verilog Adder
Dataflow Modeling (Continuous Assignment)
module fulladd(Cin, x, y, s, Cout); input Cin, x, y; output Cout, s; assign s = x ^ y ^ Cin; assign Cout (x&y) | (x & Cin) | (y&Cin); endmodule

## Slide 10: Instantiation
Module name, followed by a unique instance name and a port map phrase.
  Example:
    fulladd stage0 (carryin,x0,y0,s0,c1);
  Port map
    Connects signals from here to there
Same module may be instantiated more than once, but with a unique instance name.
The module doing the instantiation must know what the definition of the module is.

## Slide 11: Vectored Signals
Verilog provides vectors, which allow us to define signals of arbitrary width.
Example:
  input [3:0] X;
  X is a 4-bit wide signal

## Slide 12: The wire Data Type
For internal connections with no connection to an input or output port, we use the wire data type.
Don’t let the word “wire” throw you off. This is not just a conductor.
  Can drive loads!
Example:
  wire [3:1] C;
  A 3-bit wide internal signal

## Slide 13: The parameter Keyword
The parameter keyword is like a #define in C/C++. It lets you define a constant.
Example:
  parameter n = 4; wire [n-1:0] W;
  W is then a 4-bit wide signal.
  Some design houses don’t use this.

## Slide 14: The Verilog for Statement
The Verilog for is almost identical to a C/C++/Java for except:
  The unary ++ and -- operators don’t exist.
    Therefore, you must do something like: k = k + 1
  The { and } are replaced by begin and end, respectively.
Like the if statement, a for can only exist in the sequential always or initial block.

## Slide 15: Putting It All Together

## Slide 16: Different Net Types
We have talked about the wire.
The other net is the tri.
  tri wires support the Z logical value.
  Be careful with these, as they may not be synthesizable.

## Slide 17: Number Representation in Verilog
<bits>’<radix><digits>
Examples:
  4’b1101
  12’o7734
  12’hBA9

## Slide 18: What You’ll Really Do

## Slide 19: The Conditional Operator
Also called ternary operator
conditional ? true_expr : false_expr
  Example: A = (B < C) ? (A + 5) : (A + 2)
  Don’t use this thing.
  Seriously.

## Slide 20: The Case Statement
case(expression) alt1: stuff; alt2: stuff; … etc. … [default: stuff;] endcase

## Slide 21: Case Example

## Slide 22: Implementing an ALU

## Slide 23: Casex and Casez
Allows you to include the “x” and “z” logic values in your case statements.

## Slide 24: The generate Construct
Allows “on-the-fly” sub-circuit generation.
Only included in Verilog-2001 standard.
  Beware! Many tools do not yet support this.

## Slide 25: Tasks and Functions
Both act like methods in Java
Allow you to create some block of code that gets called an arbitrary number of times.

## Slide 26: Key Differences
A function shall execute in one simulation time unit; A task can contain time-controlling statements.
A function cannot enable a task; a task can enable other tasks or functions.
A function shall have at least one input type argument and shall not have an output or inout type argument; A task can have zero or more arguments of any type.
A function shall return a single value; A task shall not return a value.

## Slide 27: Lecture 9 Summary
Verilog syntax is basically like C, with some small exceptions.
Execution of Verilog code is not strictly linear.
You should make a point of being most comfortable with the behavioral coding style.