## Slide 1: EE 3173 Lecture 13
USB – The Universal Serial Bus

## Slide 2: Reading Assignment
USB and Firewire: Two Standards, Only One World – By Monday 07 April
    http://www.analogzone.com/iot_1125.pdf
    Or on Blackboard

## Slide 3: Different types of I/O Channels
USB
  v1.0, v1.1 & v2.0
Infiniband
Firewire
Ethernet
  Together with TCP/IP

## Slide 4: USB
http://www.ul.ie/~rinne/et4508/ET4508_p13.ppt More slides later
USB = Universal Serial Bus
  Industry-led open standard
USB Implementers Forum USB-IF
  Intel, Microsoft, HP, Compaq…
Evolution
  USB 1.0 (1996)
  USB 1.1 (1998)
  USB 2.0 (2000)

## Slide 5: www.usb.org
Specification freely available
Images from many locations
Most from usb.org presentations
http://www.usb.org/developers/presentations/

## Slide 6: USB Versions & Bandwidth
USB 1.X is up to 12Mb/s (FS)
  1.536KB/s in a single frame
USB 2.0 is up to 480Mb/s (HS)
  7.68KB/s in a single frame

## Slide 7: USB 1.1/2.0 Interoperability Matrix

## Slide 8: USB 2.0: What Changed?
Low level electricals for High Speed (HS) signaling
  Much higher bit rate (480Mb/s) requires new transmitter/receiver
Hub changes for backward compatibility
  Features limit bandwidth impact of Full Speed (FS) and Low Speed (LS) devices on HS devices
  FS/LS devices consume a bit-rate equivalent of HS bandwidth
    6Mb/s conferencing camera consumes 50% (6 / 12) of FS bus, but only ~2% (6 / 480) of HS bus

## Slide 9: USB Cable
Simplicity at the physical layer
All information Serial – single BIT of data
  high-speed (HS) signaling bit rate is 480 Mb/s.
  full-speed (FS) signaling bit rate is 12 Mb/s.
  limited capability low-speed signaling mode is also defined at 1.5 Mb/s.
http://www.usb.org/developers/docs

## Slide 10: 2 Types of USB Cables
High Speed Cables
  Shielded, jacketed - use twisted pair wiring
  Support max data rates of 12Mb/s
  Support Cable lengths of 5m
Low Speed cables
  Not shielded, pairs not twisted, cheaper
  Support 1.5Mb/s
  Support Cable lengths of 3m
Notes: USB supports two data rates – 12MB/s signalling requires higher specified and more expensive cabling; the lower data rate of 1.5Mb/s can be realised with lower cost cabling. The new high speed USB standard (Ver 2.0) can use the same connector and cabling hardware.

## Slide 11: Differential Current Drive

## Slide 12: USB Connectors
Power pair
Differential Signal pair
Connectors
  4-Position with shielded housing
  Positive Retention
  Blind Mating Capabilities
Cables
  28 AWG twisted pair for signaling
  20-28 AWG pair for power
  Shielding for fully rated segments
Notes: The USB connectors support blind mating in order to fulfil their ease of use requirements.

## Slide 13: Keyed Connector Protocol
The physical difference in the Series “A” and “B” connectors insures proper end user connectivity.
The “A” connector is the principle means of connecting USB devices directly to a host or to the downstream port of a hub.
  All USB devices must have the standard Series “A” connector.
The “B” connector allows device vendors to provide a standard detachable cable.
  This facilitates end user cable replacement.

## Slide 14: mini-B Connectors
The USB 2.0 specified device-side connector – the B connector – is too large for use with a new generation of handheld and mobile devices which would benefit from connectivity to the PC. Enter a “mini-B” connector.
  The new connector only applies to upstream facing ports, i.e., connectors on devices.

## Slide 15: Plugs and Receptacles
Series “A” receptacle mates with a Series “A” plug. Electrically, Series “A” receptacles function as outputs from host systems and/or hubs.
Series “A” plug mates with a Series “A” receptacle. The Series “A” plug always is oriented towards the host system.
Series “B” receptacle mates with a Series “B” plug (male). Electrically, Series “B” receptacles function as inputs to hubs or devices.
Series “B” plug mates with a Series “B” receptacle. The Series “B” plug is always oriented towards the USB hub or device.

## Slide 16: Terminations - Series A & B

## Slide 17: Terminations: mini-B

## Slide 18: Detachable Cables

## Slide 19: Captive Cables

## Slide 20: The USB Icon

## Slide 21: Why Multiple Connectors?
The series A plug is supposed to point towards the host.
If we have a cable with two series A plugs, who is the host?
  Remember, USB is really master-slave.
  Thus sayeth the spec: A cable assembly with both ends terminated in Series “A” plugs allows two downstream ports to be directly connected.
  Downstream is defined as: the direction of data flow from the host or away from the host. A downstream port is the port on a hub electrically farthest from the host that generates downstream data traffic from the hub.
As noted, mini-B exists because USB wasn’t psychic, predicting the spread of tiny USB gadgets.

## Slide 22: Device State
Only PART of the device FSM
Device must establish communication at 12 MHz before trying 480
Device state is known by IOP
127 maximum devices

## Slide 23: Disconnect Detection
Basic idea is to check for higher than normal signal voltages on the differential pair
Higher voltages will result when device terminations are removed - nominal increase is a jump from 400mV to 800mV
Check is performed during last 8 bits of EOP of uSOF frames
uSOF EOP is lengthened to 40 bits to make this mechanism reliable - duration must be longer than round-trip time of maximum length cable

## Slide 24: OSI Model

## Slide 25: USB Layers
Engineers can focus on a single layer
Function calls (nr_spi_txchar) allow simple interfacing to interrupt I/O
Three layers – will this result in lower latency than the OSI 7?

## Slide 26: USB 2.0 Software Stack
No changes Req’d for 2.0 for these SW pieces
New development work for Host Controller Driver and Hub Driver

## Slide 27: Packet Size Comparison
Control
Bulk
Interrupt
Isochronous
8, 16, 32, 64
8, 16, 32, 64
1-64
1023
64
512
1024
1024
USB 1.1
USB 2.0
Transfer type
Packet size

## Slide 28: USB Pipes
USB Communication uses the idea of a Pipe
The USB connection consists of a big pipe (12Mb/s) and up to 127 small pipes
Each of the small pipes connects to a USB device
Each small pipe can connect to a smaller pipe (tiny pipe) – up to 16 tiny pipes per small pipe
Notes: Pipes are one of the most important concepts in USB. The concept uses the analogy of a pipe used in plumbing.

## Slide 29: USB Pipes – Analogy To Physical Pipe
Notes: This slide illustrates the idea of USB pipes. Tiny pipes connect up to USB endpoints, which we will look at next.

## Slide 30: Addresses and Endpoints
USB Token has 7 address bits per USB device
Address 0 – USB Default address is used for all devices when first attached
Hence 127 USB Devices (small pipes)
4 Endpoint bits in a USB token allow up to 16 pairs of tiny pipes per small pipe
Endpoint 0 – just for Control transfers
USB Tokens also identify IN or OUT direction
15 bi-directional sources or receivers of data per USB Device – identified by Endpoints
Notes: USB uses pipes to communicate with Endpoints. Endpoints are how complex USB devices are made up. Note that Endpoint 0 is reserved for Control Transfers. At enumeration time the default connection is to Address 0, Endpoint 0.

## Slide 31: USB Pipes and Endpoints
All USB transfers occur through virtual pipes associated with Endpoints
Each Pipe may have different bandwidth and may require different types of data transfer
Each endpoint associated with a descriptor
  Type of Data Transfer
  Max size of data packets
  Interval for transfer, bandwidth needed etc
A pipe is of one of two types:
  Message -- Very structured USB-specific stuff
  Stream -- Unstructured, hey-whatever-its-cool stuff
Notes: Pipes and endpoints can have different characterists – different data transfer types and bandwidth requirements. Each endpoint has a descriptor that allows it to tell the host what its requirements are.

## Slide 32: Endpoints
Device may have a number of endpoints
E.g. Different Endpoint (and pipe) for
  Data
    File transfers – low error rate necessary
  Voice
    Error tolerant but not delay tolerant
  Control
    Low error rate but lower data rate
Notes: This example shows how a Multimedia device can be made up of several endpoints, each of which may have different data transfer and bandwidth requirements.

## Slide 33: USB Network Topology
Tiered Star Topology
Top level devices are called hubs.
Additional connectors are called ports.
Any additional functionality is called a function.
A single device may contain multiple functions!

## Slide 34: USB Flow
Logical and Physical Flow of Data through USB Wire, Endpoints and Pipes.
Data is physically transmitted through USB Wire by a Host Controller.
USB System Software consists of Host Controller drivers that enables the client software to communicate with the USB device.
USB Client Software runs on the host computer and communicates and control the USB devices through underlying layers of the USB.

## Slide 35: USB Data Transfer Types
USB supports four transfer types:
  Control Transfers: Bursty, non-periodic, host software-initiated request/response communication, typically used for command/status operations.
  Isochronous Transfers: Periodic, continuous communication between host and device, typically used for time-relevant information. This transfer type also preserves the concept of time encapsulated in the data. This does not imply, however, that the delivery needs of such data is always time-critical.
  Interrupt Transfers: Low-frequency, bounded-latency communication.
  Bulk Transfers: Non-periodic, large-packet bursty communication, typically used for data that can use any available bandwidth and can also be delayed until bandwidth is available.
Notes: USB Defines 4 types of data transfer: Control, Bulk, Interrupt and Isochronous. Each type is best suited to a particular type of data exchange.

## Slide 36: Transfer Type Control
Control
  Exchange configuration, set-up and command information between the device and the host
  CRCs are used for error checking as error-free transmission is critical
  Re-transmission initiated when errors are detected
    Re-transmission may or may not be during the current microframe.
  Control endpoints are implemented on Endpoint 0 pair
  Control transfer has 2 or 3 stages: setup stage, optional data stage, status stage
Notes: USB Defines 4 types of data transfer: Control, Bulk, Interrupt and Isochronous. Each type is best suited to a particular type of data exchange.

## Slide 37: Transfer Type Bulk
Bulk Transfers
  Large amounts of data where data is not time-critical
  Error free transfer important, hence CRC error-checking implemented
  Claim unused bandwidth when nothing more important is going on
  Typical applications: scanners, printers

## Slide 38: Transfer Type Interrupt
Interrupt
  Not interrupts in normal sense!
  Unidirectional - only inputs to the host
  Small data transfers that occur infrequently
  Host polls polls interrupt endpoints to see if they have any data to send
    Full speed devices: 1ms - 255ms polling
    Low speed devices: 10ms - 255ms
  Error checking validates the data
  Mice and keyboards

## Slide 39: Transfer Type Isochronous
Isochronous
  Unidirectional or bidirectional
  For time sensitive information, e.g. audio or video streaming
  System must be able to tolerate some errors
    No time for error checking
  Guaranteed access to USB with bounded latency
  No Retries
  Max packet size for isochronous transfer is 1023B/frame
  Max isochronous bandwidth is 8.184Mb/s

## Slide 40: Communication Layers (1)
Frame
  Time between SOF tokens = 1ms
  Consists of a series of transactions
Transfer
  One or more transactions to move data between client software and the function
Packet
  Bundle of data organised in a set format for transmission
  Types – Token, Start of Frame, Data, Handshake, HS/LS Preamble
  Typically has Control information, Data to be transferred and Error detection and correction
Notes: This slide describes the various communication layers used in USB.

## Slide 41: Frame Generation
Data is transmitted serially
SOF transmit by Controller/ Host/IOP
SOF keeps time of channel

## Slide 42: Communication Layers (2)
Transaction
  Grouping of no more than 3 packets
  Host initiates a token packet according to schedule
  PID identifies transaction type

## Slide 43: USB Packets – 4 types
Token
SOF (Start of Frame)
Data
Handshake
HS/LS Preamble (optional)
All packets have
  Sync field to lock the Phase Locked Loop
  Followed by Packet Identifier (PID)
  Also address, frame number or data
Packet
  Bundle of data organized in a known format for transmission
  Typically has Control information, Data tobe transferred and Error detection and correction

## Slide 44: Token Packet

## Slide 45: Packet Identifier
Packet Type | PID Name | PID[3:2] | PID[1:0]
Token Token SOF Token | OUT IN SOF Setup | 00 10 01 11 | 01 01 01 01
Data Data | Data0 Data1 | 00 10 | 11 11
Handshake Handshake Handshake | ACK NAK STALL | 00 10 11 | 10 10 10
Special | PRE | 11 | 00

## Slide 46: SOF Packet
SOF packets are sent by the host once every 1.00ms +/- 0.05ms

## Slide 47: Data Packet
Devices respond to requests from the Host
Host sends an IN and device endpoint responds with a packet OR
Host sends an OUT followed by a data packet
Bulk, Control, Interrupt: host responds with an Acknowledge
Isochronous: no handshake packet

## Slide 48: Handshake Packet
Special Packet
Host sends a PRE (preamble) packet when it wants to communicate with 1.5Mb/s devices

## Slide 49: USB Frame Model

## Slide 50: Isochronous SW Interface
Packet-oriented interface
Each I/O Request includes:
Reference to a virtually contiguous data buffer
Array of packet info/status
  Input: per packet buffer offset
  Output: per transaction results
  Each element maps to one USB Frame (1 ms)
Minimum sized request buffer is one packet

## Slide 51: USB: Explicit Timeshare
Enables QoS
Example of Devices Sharing USB Bandwidth During a Single Frame
  Isochronous Transfer
  Interrupt Transfer
  Control Transfer
  Bulk Transfer

## Slide 52: USB 2.0 Dual Terminations
Dual Termination Makes USB 2.0 Speeds Possible on USB 1.X Cable Assemblies
Simulation assumes ideal transceivers and terminations
Typical imperfections are modeled for cable, connectors, bond wires, etc.
2.7X increase in eye opening, 2.7X decrease in jitter
Single Termination
Dual Termination

## Slide 53: Integrated ASIC USB Solution
ARM7TDMI
Core
USB 1 Port
5K bytes
SRAM
130K Gates
Logic

## Slide 54: Where to from here?
USB On-The-Go
  Allows USB connections without a host.
  Direct competition with FireWire.
Wireless USB
  480 Mbps at 3m, 110 Mbps at 10m.
  Otherwise is normal USB.
USB 3.0
  SuperSpeed -- 4.8 Gbps. Demonstrated late 2008, spec available “soon”, commercial devices in 2009 or 2010.
  Supposedly adds another differential pair specifically for SuperSpeed transmissions, while retaining familiar USB connector shape.

## Slide 55: One Last Amusement
“There are an increasing number of devices that could potentially take advantage of the additional bandwidth, including external hard drives, flash readers, video cameras, and the all-new USB-compliant llama expected to be genetically delivered from the Andes sometime in late 2011. Obviously a USB llama wouldn't be much use without a USB 3.0 device—ever tried downloading from a llama over an old 10BaseT network? Yeah. It'd be worse.”
    Joel Hruska, “Ars Technica”, 17 September 2007
http://arstechnica.com/news.ars/post/20070918-intel-announces-demonstrates-usb-3-0.html

## Slide 56: Lecture 13 Summary
USB is a modern serial communications protocol that is cheap but effective.
Features:
  Packet-based interface
  Master-slave arbitration
  Differential current signaling
  Low Speed, Full Speed, High Speed
  Pipes
  Up to 127 devices on a given bus