## Slide 1: EE 3173 Lecture 11
Chapter 7 – Input/Output

## Slide 2: Chapter 7 Concepts
Input/Output
  Making the external bus hierarchy work
  Block Diagrams
  Memory Maps
    System
    Device control registers
  I/O Programming models
    Polled / Programmed I/O
    Interrupt I/O
    DMA I/O

## Slide 3: Input/Output Problems
Wide variety of peripherals
  Delivering different amounts of data
  At different speeds
  In different formats
All slower than CPU and RAM
Need I/O modules

## Slide 4: External Devices
Human readable
  Screen, printer, keyboard
Machine readable
  Monitoring and control
  A2D, D2A
Communication
  UART
  Modem
  Network Interface Card (NIC)

## Slide 5: Typical I/O Data Rates

## Slide 6: Where to Draw the Box?
Input/Output – of What?
  Based on perspective/context of use
  Complex systems are Partitioned at many levels
    Core/IP designer
    Chip/System-on-a-Chip designer
    System/Chassis designer
    Software designer
  In this Class – I/O refers to either:
    Input/Output to/from the Nios processor core
      Not necessarily off the FPGA
    The study of I/O operations and classifications

## Slide 7: Generic Model of I/O Module

## Slide 8: External Device Block Diagram

## Slide 9: I/O Module Function
Control & Timing
CPU Communication
Device Communication
Data Buffering
Error Detection

## Slide 10: I/O Module Diagram

## Slide 11: I/O Hardware Model
Input Port:
  Receives data from the incoming pins
  Makes it available to the data bus
  Generally does not latch the data
Output Port:
  Receives data from the data bus
  Makes it available on the outgoing pins
  Usually has a latch to hold the data for the device
  Value remains constant until a new value is output

## Slide 12: I/O Synchronization
I/O Speed
  I/O devices are typically much slower than processors
  Can’t read from a device until it has the data ready
  Can’t write to a device until it is ready to receive data
    Usually when it is done processing the previous data
Processor must “synchronize” with I/O devices
  Device sets a 1-bit “ready” flag when it is ready
  Processor waits for flag to be set before accessing the port
  Flag is cleared when processor accesses the port

## Slide 13: I/O Module Decisions
Hide or reveal device properties to CPU
Support multiple or single device
Control device functions or leave for CPU
Also O/S decisions
  e.g., Unix treats everything it can as a file

## Slide 14: Command & Status Register
Flag is usually 1 bit of a “Command & Status Reg”
This register is part of the I/O port
It will have a different address than the data port
Purposes:
  Allow processor to read status info on the port
    e.g. Ready, Error, etc
  Allow the processor to write commands to the port
    To alter the way the port behaves

## Slide 15: Typical I/O Port

## Slide 16: Nios I/O Control Registers
Each control register for the I/O device is mapped into the address space
Allows for flexible operation
  Polled or Interrupt I/O

## Slide 17: I/O Addressing
Typically, it is convenient to assign a part of the address space to I/O devices.
  All I/O devices must use that subset of addresses
Example, let 0x1000 - 0x103F be reserved for I/O
  Allows 26 = 64 unique I/O addresses
  More than usually needed
Address Decoding
  How to generate a unique enable/select for each device on the bus
  Bus is a common/shared resource – address uniquely identifies location or memory

## Slide 18: Nios Memory Map

## Slide 19: Three forms of I/O
Polled/Programmed I/O
  Processor enters a “polling loop” to read the ready flag
  When the flag is set, then processor accesses port
  Processor ends up waiting for the device
Interrupt-Driven I/O
  Ready flag is connected to an “Interrupt” pin on processor
  When Pin = 1, the processor
    Interrupts the current program
    Calls an Interrupt Service Routine (ISR) to access the port
    Returns to the previous program
DMA (Direct Memory Access)
  ISR supports control of an independent bus master

## Slide 20: I/O Synchronization
I/O Synchronization is determined by the programming model
  Polled
  Interrupt
  DMA
I/O Synchronization is constrained by interface hardware between CPU/Controller and I/O Controller/Devices

## Slide 21: Input of a Block of Data

## Slide 22
Spectrum of I/O Data Transfer Methods
Polling
DMA
Interrupt-driven
(Single bus system assumed)
--- low data
rates
--- highest data
rates
--- moderate data
rates
--- no special
hardware
required
--- intelligent I/O
or DMA con-
troller required
--- hardware support
provided in most
standard CPUs
--- usually
wastes
CPU cycles
--- fewest CPU
cycles
required
--- may require
many CPU
cycles for
data transfers
--- software can be
tricky to design
and debug
--- simple
looping
software
--- must avoid
interactions
with cache
and virtual
memory

## Slide 23: Polled I/O Steps
CPU checks I/O module device status
I/O module returns status
If ready, CPU requests data transfer
I/O module gets data from device
I/O module transfers data to CPU
Variations for output, DMA, etc.

## Slide 24: Polled/Programmed I/O
CPU has direct control over I/O
  Sensing status
  Read/write commands
  Transferring data
CPU waits for I/O module to complete operation
Wastes CPU time

## Slide 25: Programmed I/O - Detail
CPU requests I/O operation
I/O module performs operation
I/O module sets status bits
CPU checks status bits periodically
I/O module does not inform CPU directly
I/O module does not interrupt CPU
CPU may wait or come back later

## Slide 26: Interrupt Driven I/O
Overcomes CPU waiting
No repeated CPU checking of device
I/O module interrupts when ready

## Slide 27: Interrupt-Driven I/O
CPU issues read command
I/O module gets data from peripheral whilst CPU does other work
I/O module interrupts CPU
CPU requests data
I/O module transfers data

## Slide 28: Interrupt Processing

## Slide 29: CPU Viewpoint
Issue read command
Do other work
Check for interrupt at end of each instruction cycle
If interrupted:-
  Save context (registers)
  Process interrupt
    Fetch data & store
See Operating Systems notes

## Slide 30: Design Issues
How do you identify the module issuing the interrupt?
How do you deal with multiple interrupts?
  i.e. an interrupt handler being interrupted

## Slide 31: Identifying Interrupting Module
Different line for each module
  PC
  Limits number of devices
Software poll
  CPU asks each module in turn
  Slow

## Slide 32: Identifying Interrupting Module
Daisy Chain or Hardware poll
  Interrupt Acknowledge sent down a chain
  Module responsible places vector on bus
  CPU uses vector to identify handler routine
Bus Master
  Module must claim the bus before it can raise interrupt
  e.g. PCI & SCSI

## Slide 33: Multiple Interrupts
Each interrupt line has a priority
Higher priority lines can interrupt lower priority lines
If bus mastering only current master can interrupt

## Slide 34: Direct Memory Access
Interrupt driven and programmed I/O require active CPU intervention
  Transfer rate is limited
  CPU is tied up
DMA is the answer

## Slide 35: DMA Function
Additional Module (hardware) on bus
DMA controller takes over from CPU for I/O

## Slide 36: Direct Memory Access
Interrupt driven and programmed I/O require active CPU intervention
  Transfer rate proportional to CPU overhead
  PARALLELISM provides performance
    Dual processor – DMAC
    Pipelining & superscalar
DMA requires Additional Module (hardware) on bus
DMA controller takes over from CPU for I/O

## Slide 37: DMA Operation
CPU tells DMA controller:-
  Read/Write
  Device address
  Starting address of memory block for data
  Amount of data to be transferred
CPU carries on with other work
DMA controller deals with transfer
DMA controller sends interrupt when finished

## Slide 38: DMA Transfer Cycle Stealing
DMA controller takes over bus for a cycle
Transfer of one word of data
Not an interrupt
  CPU does not switch context
CPU suspended just before it accesses bus
  i.e. before an operand or data fetch or a data write
Slows down CPU but not as much as CPU doing transfer

## Slide 39: General Microcomputer with DMAC

## Slide 40: New DMA-related Signals
Request: Used by peripheral controller to inform DMAC that a DMA transfer is required.
Ack: Used by DMAC to inform peripheral controller that DMAC has control of the system bus and that a new DMA bus cycle is starting.
Ready: Handshake line from peripheral controller to DMAC to indicate that present word has been transferred.
Done: Asserted by DMAC after the entire DMA transfer is completed.
DMA Request: Asserted by DMAC to get control of the system bus from the CPU.
DMA Grant: Asserted by the CPU to pass control of the system bus over to the DMAC.
IRQ: Asserted by DMAC to alert CPU as to the end of the DMA transfer.

## Slide 41: Generic DMA Protocol
Peripheral to Memory

## Slide 42: Generic DMA Protocol
Memory to Peripheral

## Slide 43
Representative DMACs
DMAC
CPU
Number of
Channels
Data
Chaining
Max.
Transfer
Rate
Addressing
Capability
i82380
80386
32
32
Yes
8
Signetics
SCB68430
68000
5 ?
24
Yes
1
i82258
80286
8
24
Yes
4
Intel
i8237
8086
16
Yes
4
1.6
MC6844
6800
2 MB/s
16 bits
Yes
4
MC68440
68000
5
24
No
2
MC68450
68000
5
24
Yes
4

## Slide 44: DMA Configurations (1)
Single Bus, Detached DMA controller
Each transfer uses bus twice
  I/O to DMA then DMA to memory
CPU is suspended twice

## Slide 45: DMA Configurations (2)
Single Bus, Integrated DMA controller
Controller may support >1 device
Each transfer uses bus once
  DMA to memory
CPU is suspended once

## Slide 46: DMA Configurations (3)
Separate I/O Bus
Bus supports all DMA enabled devices
Each transfer uses bus once
  DMA to memory
CPU is suspended once

## Slide 47: Lecture 6 Summary
Various I/O Challenges
I/O Synchronization
  Polled
  Interrupt
  DMA
DMA Nitty-Gritty