## Slide 1: EE 3173 Lecture 12
More IO Processing

## Slide 2: Lecture 7 Concepts
IO Programming -- Adding some intelligence to I/O.
Representative samples and case studies.
  x86 interrupts
  Intel 8237A DMAC
I/O Channels

## Slide 3: Example - PC Bus
Many devices had companion devices
  Becoming less common as we are able to place more complexity on a single device
  Now more commonly elements of a SoC – chipset, host controller, etc
8259A - 80x86 interrupt controller
  8086 device has one interrupt line
  8086 based systems can use one or more 8259A interrupt controllers
  8259A enables 8 separate interrupt lines IRQ1-8
8237A - 80x86 DMA controller
  80x86 does not have a built in DMA controller
  The 8237A is one DMA Controller for the PC Bus
8089 – 80x86 IO processor
  A full coprocessor to offload I/O processing
  The predecessor to the modern “IO Channel”
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: Sequence of Events
8259A accepts interrupts
8259A determines priority
8259A signals 8086 (raises INTR line)
CPU Acknowledges
8259A puts correct vector on data bus
CPU processes interrupt
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: 82C59A Interrupt Controller
ISA bus chains two 8259As together
Link is via interrupt 2
Gives 15 lines
  16 lines less one for link
IRQ 9 is used to re-route anything trying to use IRQ 2
  Backwards compatibility
Incorporated in chip set
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Intel 82C55A – Interface device
Parallel I/O device
Adds parallel ports into the I/O memory map

## Slide 7: Intel 8237A DMA Controller
Interfaces to 80x86 family and DRAM
When DMA module needs buses it sends HOLD signal to processor
CPU responds HLDA (hold acknowledge)
  DMA module can use buses
Example: Transfer data from memory to disk
  Device requests service of DMA by pulling DREQ (DMA request) high
  DMA puts high on HRQ (hold request),
  CPU finishes present bus cycle (not necessarily present instruction) and puts high on HDLA (hold acknowledge). HOLD remains active for duration of DMA
  DMA activates DACK (DMA acknowledge), telling device to start transfer
  DMA starts transfer by putting address of first byte on address bus and activating MEMR; it then activates IOW to write to peripheral. DMA decrements counter and increments address pointer. Repeat until count reaches zero
  DMA deactivates HRQ, giving bus back to CPU

## Slide 8: 8237 DMA Usage

## Slide 9: 8237 Overview
While DMA using buses processor idle
Processor using bus, DMA idle
  Known as fly-by DMA controller
Data does not pass through and is not stored in DMA chip
  DMA only between I/O port and memory
  Not between two I/O ports or two memory locations
Can do memory to memory via register
8237 contains four DMA channels
  Programmed independently
  Any one active
  Numbered 0, 1, 2, and 3

## Slide 10: I/O Channels
I/O devices getting more sophisticated
  e.g. 3D graphics cards
CPU instructs I/O controller to do transfer
I/O controller does entire transfer
Improves speed
  Takes load off CPU
  Dedicated processor is faster
Notes: <number>
<footer>
<header>
<date/time>

## Slide 11: I/O Channel Architecture
I/O Channel or I/O Processor (IOP)
  Smart, programmable DMA Controller
  A processor customized for I/O operations
    I/O-specific instruction set
    I/O-specific register architecture
Attributes
  More flexible than "dumb" DMA controller
    Services more I/O devices
    Services a wider variety of I/O devices at one time
  Has more control over I/O operations
  Can handle more complex data transfers

## Slide 12: CPU - IOP Interactions
Most CPU - IOP communication
  is passed via messages left in main memory
  uses pre-agreed memory locations
CPU initiates an I/O operation by:
  storing the starting address of the IOP program
  storing parameters the IOP will need
  issuing and attention signal (ATT) to wake up IOP
IOP then executes the I/O operation by:
  fetching the I/O program address from memory
  loading it into its own Program Counter (PC).
  executing the I/O program (including any DMA)
  issuing a completion INTR to the CPU

## Slide 13: I/O Channel Architecture
Typically, CPU and IOP share same memory space
Significant Bus Contention between processors
  CPU instr & data + DMA + IOP instr & data

## Slide 14: Dual-Bus Channel Architecture
Reduces Traffic on System Bus
IOP can manage two memory spaces as two partitions of a single address space

## Slide 15: IOP Instruction Set
Customized to I/O Instructions
  Arithmetic Instructions:
    No floating point
    Limited fixed-point instructions for address calculations
  General I/O instructions
    To set-up and clean-up before and after transfer
    To initiate DMA transfer (e.g. READ, WRITE, XFER)
    Note: DMA must be hardware-implemented
  Device Specific Instructions
    For comm. with devices (e.g. REWIND, SEEK, PRINT_LINE)

## Slide 16: Relevant CPU Instruction Set
May be Sufficient to have one instruction
  Asserts the ATT signal
  All I/O parameters must have been previously stored
May be more Efficient with special I/O instructions
  e.g. START-IO, HALT-IO, TEST-IO
  Each I/O instruction would:
    Place IOP address on Address bus
    Place IOP command on Data bus
    Assert ATT line
  More useful in CPU designed for mainframe system

## Slide 17: Case Study: Intel 8089 IOP
Companion to 8086 CPU (old, simple, documented)
Has 2 parallel IOP's (a.k.a. Channels) on 1 chip
  Some resources are shared between the 2 channels
Notes on 8086 bus architecture
  Addr. & Data time-multiplexed on same physical lines
    Address = [A19... A0]  20 bits  1 MB
    Data = [D15 ... D0] = [A15 ... A0]  16 bits
  Word-size translation
    CPU operates with 16-bit words
    Many I/O devices are byte-oriented (=> 8-bit words)
    IOP must translate word-size if required

## Slide 18: 8089 Major Internal Components
Instruction Fetch Unit and Control Section
20-bit integer ALU for address calculations
Two DMA Channels (IOP's)
  CA = Channel Attention (ATT) signal
  SEL = Channel Select signal
Assembly / Disassembly: 8-bit - 16-bit conversions
Bus Interface Unit (BIU)
  One BIU can handle dual-bus system architecture
  Need external latches and MUXes to separate busses
  Uses Highest Order address bit to discriminate busses

## Slide 19: 8089 Block Diagram

## Slide 20: CPU - IOP Communication
CPU-IOP communication:
  through shared data structures in main memory
  1 8086 “word” = 16 bits
8086 / 8089 shared data structures
  CCB = Channel Control Block (4 words per channel)
    Parameter Block (PB) Pointer (2 words)
    Channel Status Word (1 word)
    Channel Command (1 word)
  CPB = Channel Parameter Block (variable length)
    IO program pointer = address of I/O pgm (2 words)
    IO program parameters (as many as needed)

## Slide 21: CPU-IOP Communication

## Slide 22: CPU-IOP Communication
Example:
  Channel 1: screen update execution & keyboard input
  Channel 2: screen buffer & floppy drive control

## Slide 23: Register Architecture
Main Addressing Registers

## Slide 24: Register Architecture
Control Registers

## Slide 25: Register - Data Structure Relationships

## Slide 26: 8089 DMA Mode Operation
DMA Mode initiated by “XFER” instruction
  Suspends instruction fetch-execute cycle
  Turns control over to hard-wired DMA controller
  DMA controller handles the actual data transfer
DMA terminated by conditions defined in CC register
  Single transfer (1 Byte)
  Terminate when byte count = 0
  Wait for external "terminate" signal
  Terminate on (masked) comparison
    Based on actual data stream
    Allows IOP to detect special symbols (e.g. EOF)

## Slide 27: 8089 Masked Comparison
Example: Want to terminate I/O transfer at EOF
  EOF = ASCII <cntl>Z
    ASCII = 7-bit code with optional 8th parity bit
  Before entering DMA mode:
    pre-load <cntl>Z into COMPARE register
    load MASK register to ignore high-order (parity) bit
  While in DMA mode:
    Compare each byte transferred to the COMPARE reg.
    Terminate DMA if :
      masked data value = masked COMPARE reg.

## Slide 28: Overview of 8089 Operation
High Level Sequence of events Power Up Initialization wait: Wait for CA and SEL signals Read program start-up parameters from CCB Enter program mode (= Task Block (TB) mode) Enter DMA Mode (do I/O transfer) Return to program mode (exec more program) Store status value go to wait

## Slide 29: 8089 State Diagram
Allows for two simultaneous DMA transactions
Much simpler than the FSM for a CPU
Each DMAC is going to have a similar but different functionality
  Instruction set
  Block size
  Address space

## Slide 30: 8089 Instructions of Interest
XFER = Switch to DMA mode hardware controller
  Stop fetching and executing instructions
  Turn control over to hardwired DMA controller
  Executes one more instruction before switching
    XFER delay slot (like a TRAP delay slot)
HALT = Return to wait state (end program mode)
SINTR = Issue completion INTR signal to CPU
  Not done automatically on HALT
  Must use SINTR in program before HALT

## Slide 31: Lecture 12 Summary
IOP (Channel) = Special Purpose Processor
  ISA customized for IO operations
  Built-in hard-wired DMA Controller
CPU - IOP Interactions
  Shared memory area
  CPU
    stores command, pgm address, parameters
    issues ATT signal
  IOP
    reads stored info & executes IO program
    stores status of IO operation
    issues completion INTR