## Slide 1: EE 3173 Lecture 5
Chapter 3

## Slide 2: Chapter 3
Into Chapter 3
    Description of the proc-based system as an interconnection of functional blocks
High level view of Computer Function & Interconnection
    Interrupt sequencing
    Fundamental Components & interconnections
    PCI
    Other bus technology examples
Supplemental Reading
    www.pcguide.com/ref/mbsys/buses/
    www.pcguide.com/

## Slide 3: Computer Components
All computers have:
  CPU
  Memory
  I/O
  Interconnect
One view of a CPU

## Slide 4: Interrupts
Mechanism by which other modules (e.g. I/O) may interrupt normal sequence of processing
Program
  e.g. overflow, division by zero
Timer
  Generated by internal processor timer
  Used in pre-emptive multi-tasking
I/O
  from I/O controller
Hardware failure
  e.g. memory parity error

## Slide 5: Interrupt Cycle
Added to instruction cycle
Processor checks for interrupt
  Indicated by an interrupt signal
If no interrupt, fetch next instruction
If interrupt pending:
  Suspend execution of current program
  Save context
  Set PC to start address of interrupt handler routine
  Process interrupt
  Restore context and continue interrupted program

## Slide 6: Transfer of Control via Interrupts

## Slide 7: Instruction Cycle with Interrupts

## Slide 8: Multiple Interrupts
Disable interrupts
  Processor will ignore further interrupts whilst processing one interrupt
  Interrupts remain pending and are checked after first interrupt has been processed
  Interrupts handled in sequence as they occur
Define priorities
  Low priority interrupts can be interrupted by higher priority interrupts
  When higher priority interrupt has been processed, processor returns to previous interrupt

## Slide 9: Multiple Interrupts - Sequential

## Slide 10: Multiple Interrupts – Nested

## Slide 11: Time Sequence of Multiple Interrupts

## Slide 12: Interconnection
All the units must be connected
Different type of connection for different type of unit
  Memory
  Input/Output
  CPU

## Slide 13: Computer Modules
Each Module has Inputs and outputs
Some signals are shared I/O (typically data)
These functional blocks are used in:
  System Level Diagrams
  Quartus Block Diagrams
  Describing the functional Units

## Slide 14: Memory Connection
Receives and sends data
Receives addresses (of locations)
Receives control signals
  Read
  Write
  Timing

## Slide 15: Input/Output Connection
Similar to memory from computer’s viewpoint
Output
  Receive data from computer
  Send data to peripheral
Input
  Receive data from peripheral
  Send data to computer

## Slide 16: Input/Output Connection
Receive control signals from computer
Send control signals to peripherals
  e.g. spin disk
Receive addresses from computer
  e.g. port number to identify peripheral
Memory Mapped I/O
  I/O devices are addressed through conventional Load/Store instructions to the normal address space
Separate I/O address space
  Separate I/O instructions access an I/O device only address space

## Slide 17: CPU Connection
Reads instruction and data
Writes out data (after processing)
Sends control signals to other units
Receives (& acts on) interrupts

## Slide 18: Buses
There are a number of possible interconnection systems
Single and multiple BUS structures are most common
e.g. Control/Address/Data bus (PC)
e.g. Unibus (DEC-PDP)

## Slide 19: What is a Bus?
A communication pathway connecting two or more devices
Usually broadcast
Often grouped
  A number of channels in one bus
  e.g. 32 bit data bus is 32 separate single bit channels
  And frequently, 32 individual conductors
Power lines may not be shown

## Slide 20: Bus Interconnection Scheme
What do buses look like?
  Big and Yellow with wheels
  Parallel lines on circuit boards
  Ribbon cables
  Strip connectors on mother boards
    e.g. PCI
  Sets of wires

## Slide 21: Data component
Carries data
  Remember that there is no difference between “data” and “instruction” at this level
Width and switching frequency are key determinants of performance
  Asynchronous vs. synchronous
  8, 16, 32, 64 bit
  33, 100, 166 MHz
  Double Data Rate

## Slide 22: Address Component
Identify the source or destination of data
e.g. CPU needs to read an instruction (data) from a given location in memory
Bus width determines maximum memory capacity of system
  e.g. 8080 has 16 bit address bus giving 64 kbyte address space
  Nios uses a 32 bit address space, providing for a 4 Gbyte address space

## Slide 23: Control component
Control and timing information
  Clock signals
  Reference voltages
  Memory read/write signal
  Parity or Correcting Code
  Interrupt request

## Slide 24: Single Bus Problems
Lots of devices on one bus leads to:
  Propagation delays
    Long data paths mean that co-ordination of bus use can adversely affect performance
    If aggregate data transfer approaches bus capacity
Most systems use multiple buses to overcome these problems

## Slide 25: Bus Types
Dedicated
  Separate data & address lines
Split –Transaction
  Between REQ_A and RSP_A the bus can be used for other activities.
Multiplexed
  Shared lines
  Address valid or data valid control line
  Advantage - fewer lines
  Disadvantages
    More complex control
    Ultimate performance

## Slide 26: Traditional (ISA) (with cache)

## Slide 27: High Performance Bus

## Slide 28: Multi-Bus Hierarchies
Limits the size of each bus
  Longer/larger busses have higher capacitance
  Increases the aggregate bandwidth
  Reduces the cost of devices on slow busses
  Enables increased performance in critical or point-to-point busses

## Slide 29: Workstation Bus Architecture
Conceptual diagram for workstation bus architecture
North/South bridge by convention only
Each bus has a throughput associated.
Higher level busses (FSB) should be capable of handling the combined bandwidth of lower busses

## Slide 30: Front Side Bus
Processor | Chipset | FSB Freq | FSB BandWidth
Pentium 4 (northwood) | Intel 845 Via P4X333 | Clock 133 MHz Data 533 MHz | 4.2 GB/s
Athlon (thoroughbred) | Via KT400 | Clock 166 MHz Data 333 MHz | 2.66 GB/s
Pentium 3 | Intel 815 | 133 (x1) | 1.064 GB/s
Each bus is unique
  To a processor or a N.Br & S.Br chipset
Requirement to have differing BW levels
Bandwidth of DRAM interface is RH bus

## Slide 31: What is a Chipset
Interconnecting “glue logic”
Determines “feature set” of motherboard
    DRAM types
    Hard drive types
Does not completely determine performance
    Typically has a maximum processor frequency
Chipset Designation | Intel 850 | Intel 815 | AMD 760 | Via KT266A | Nvidia nForce 420D | SiS 645
Processor Form | Pentium 4 Intel Socket 423 or 478 | Pentium 3 Intel FC-PGA (370 pin) | Athlon Socket A/462 | Athlon Socket A/462 | Athlon Socket A/462 | Pentium 4
Features | Dual Rambus Channels | Integrated Graphics | First DDR266 Chipset |  | Integrated GeForce2 Graphics Dual DDR Busses | Supports DDR333 (PC2400)

## Slide 32: AMD 760 Chipset Specifically

## Slide 33: Server Bus Hierarchy
DRAM controller on CPU
Hypertransport – more later
Multiple Paths for data - parallelism

## Slide 34: Timing
Coordination of events on bus
Asynchronous
  No clock signal to synchronize events
Synchronous
  Events determined by clock signals
  Control Bus includes clock line
  All devices can read clock line
  Usually a single cycle for an event
Isochronous
  Variable amount of data in sequence of fixed size packets at regular intervals
  Reduced overhead
  Desired outcome: Quality of Service

## Slide 35: Synchronous Timing Diagram

## Slide 36: Asynchronous Timing – Read Diagram

## Slide 37: Asynchronous Timing – Write Diagram

## Slide 38: Isochronous Timing
In network theory isochronous means constant time (as in constant time between packets).
In sampling theory isochronous sometimes means at the same time.
Notes: 35
35

## Slide 39: Bus Arbitration
DEF: The process of selecting a new bus master.
Participants
  Bus Control Unit (BCU)
    Central Arbiter of Bus Ownership
    May or may not be CPU
  Bus Units
    All devices which could be the bus master
3 basic control signal types
  REQ = Bus Request. (Bus Unit to BCU)
  GNT = Bus Grant. (BCU to Bus Unit)
  BSY = Bus Busy. (Current Master to BCU)

## Slide 40: Centralized Arbitration
Single hardware device controlling bus access
  Bus Controller
  Arbiter
May be part of CPU or separate
Only appropriate in constrained systems
  i.e. 2 ATA devices or 16 SCSI devices

## Slide 41: Distributed Arbitration
Each module may claim the bus
  Assert a # of wired-or signals on the bus in cycle N to determine device granted access in cycle N+1
Control logic on all modules
  Costly
  Difficult to manage – low priority device can be starved
Typical
  Point-to-point
  Managed with a multi-bus hierarchy
  When necessary # of masters is constrained

## Slide 42: General Arbitration Sequence
Bus Unit asserts REQ (asks for ownership)
When BSY is clear, the BCU
  Decides which unit shall receive mastership
  Issues GNT to only the one chosen Bus Unit
    Independent Request Method
    Poll Counter Method
    Daisy Chain method
When Chosen Unit receives GNT, it
  asserts BSY (announcing its ownership)
  Acts as bus master for one or more transfers
When finished, Unit clears BSY, (relinquishing bus)

## Slide 43: Independent Request Arbitration
Have N possible masters (bus units)
Use N independent REQ and GNT lines
  One per bus unit
Single Shared BSY line
  "Wired-OR"  if ANY unit asserts 1 then BSY = 1

## Slide 44: Independent Request Properties
Advantages
  Immediate Response from BCU
  Priorities Completely Arbitrary and Programmable
  Very Simple Bus Unit Control
  Only 3 pins / bus unit
Disadvantages
  O(N) pins on BCU
  O(N) bus lines for REQ and GNT
  Bounds N to small number

## Slide 45: Poll Counter Arbitration
Replace N REQ lines with one shared REQ line
Replace N GNT lines with "Poll Counter" lines
  Poll Counter in BCU outputs unit addresses (1..N)
  Unit takes bus when it sees own address on poll lines
  BCU cycles through addresses until it receives BSY

## Slide 46: Number of Poll Lines
Problem:
  Prevent Units from seeing transients as valid address
Solutions
  Synchronous Bus
    need a "null" address
    use bus clock to separate changing counter and sensing poll lines (e.g. opposite edges)
    Total lines for polling
  Asynchronous Bus
    Need a one-bit "count valid" signal
    Can get away without null address
    Total lines for polling

## Slide 47: Poll Counter Properties
Advantages
  O (log N) pins on BCU
  O (log N) bus lines -- Not bad, even for large N
  Can be fair
    Don't reset counter after BSY is cleared
    Avoids starvation of higher numbered units
  Variable priorities -- can alter counter sequence
Disadvantages
  N bounded by number of poll lines
  O(log N) pins / bus unit
  delay while cycling through addresses (bus propagation delay)

## Slide 48: Daisy Chain Arbitration
Common (shared) REQ and BSY lines (1 each)
Single GNT line exits BCU
  Passed from unit-to-unit (= Daisy Chain)
  Each Unit has GNT-IN and GNT-OUT pins

## Slide 49: Daisy Chain Arbitration
BCU Grant Issuance Protocol
  IF (REQ = T) AND (BSY = F) THEN assert GNT
Bus Unit Grant Passing Protocol
  IF (This Unit has NO outstanding request) THEN GNT-OUT := GNT-IN (pass GNT to next unit) ELSE GNT-OUT := False (deny GNT to next unit)
Thus, if there are multiple outstanding requests, the unit wired closest to the BCU will get GNT

## Slide 50: Daisy Chain Properties
Advantages
  Only 3 control lines (independent of N)
  Only 3 pins / BCU
  Only 4 pins / bus unit
  Trivially simple BCU
Disadvantages
  1 faulty unit can disable all "downstream" units
  Delay while GNT ripples down the line
  Unit Priorities hardwired  possible starvation of lower priority units

## Slide 51: Chapter 3 Summary
Interrupts: Changing the flow of the program
  How do we deal with multiple interrupts?
    Either we don’t, or we impose a priority scheme.
Hardware Elements need to talk to each other. Each element has its own interface.
Buses
  Connect Hardware Elements together.
  Can be asynchronous, synchronous or isochronous.
  Somebody needs to assert ownership of the bus. How does that happen?
    Daisy Chain
    Poll Counter
    Independent Request
  All of these have pros and cons.